ECE486/586 – PDP8 Simulator Report
Sean Koppenhafer, Ken Benderly, Luis Santiago, Steve Peirce

General Design Specifications
Our PDP8 simulator uses the octal format of output from the PAL assembler. Our simulator has a starting address of 0200 octal when executing programs. The simulator can run in the terminal, or in a GUI debugger. To build the terminal based simulator, build with makefile. To build the GUI based simulator, build with makefile.gui. Make clean must be done before switching to the other version.

Memory layout was implemented as an array of 16-bit, unsigned integers, (uint16_t). The number of entries was sized as [PAGES * WORDS_PER_PAGE] with PAGES and WORDS_PER_PAGE defined as 32 and 128, respectively. These values are consistent with the PDP-8 and it's 4KB of memory. Since only 12 of the 16 bits, (per index) were used, we were able to “shoe-horn” some functionality into the remaining 4 bits, such as the valid, breakpoint and tracepoint bits. When writing to memory, the page and offset were determined by masking the value to convert with 0xF80 and 0x07F, then adding the values together, completing the new, converted value. This new, converted value is used as the index into the memory array. Once indexed, we then write this value to the tracefile and preserve the extra state bits. For debugging of the code the address and computed values can be printed to the terminal by defining MEMORY_DEBUG.

Effective Address Calculation
The function takes in an instruction and places the effective address in the CPMA register as output. A 12 bit instruction and a pointer to the registers structure are passed as arguments to the effective address calculation function. The function tests bit 3 of the instruction to determine if it is a direct or an indirect mode instruction. Next it tests bit 4 to determine if the instruction is in the current page or in zero page. If the instruction is direct mode, current page, the offset in the instruction is concatenated with the current page and the value placed on the CPMA register. Similarly, for a direct mode zero page instruction, only the offset from the instruction is placed in the CPMA. If indirect mode is detected the same steps are taken to determine the value but instead of placing the value directly to the CPMA register, the value is used to do a memory read and the value from the memory read it is placed in the CPMA. Indirect address has one more feature. If the address to be used for indirect mode is stored between address 10 and 17 octal, the memory value is incremented with each access and the incremented value is used for a memory read. The memory read value is then placed in the CPMA.

To test the function we wrote a program that used all 5 addressing modes and also tested the entire range of auto increment addresses. A second version of the previous program was slightly modified to ensure auto increment only happens when indirect addressing mode is used.

Testing
We tried to test all possible edge case scenarios. For the non micro instructions, there is a test case for each instruction. The only somewhat challenging test is the TAD test, since there are many edge cases. In the TAD test, carry and non-carry situations were generated to test if link register functionality worked correctly. Micro instruction tests were divided into group 1 and group 2. Group 1 micro instructions were tested for each level to be completed in order and in combinations that combined levels of instructions. Group 2 micro instructions were tested as OR group or AND group skip level one instructions with and without other instruction levels. The OR and AND group micro instructions were tested for all possible combinations of one, two, or three skip combinations either triggering or not triggering the skip.

I/O Implementation
To implement truly non-blocking I/O, we had to make our simulator multi-threaded. One thread executes the simulator, while the other thread grabs keyboard input as is it received. Because both threads begin running at the same time, keyboard input can be entered throughout the simulators execution. The input will have no effect unless the simulator thread is currently executing an instruction that checks if the keyboard is receiving input.

All I/O instructions have been implemented, but only the krb, ksf, tsf and tls opcodes have been tested. The ~ character is special. The ~ character is not grabbed by the krb opcode to allow for testing of “missing” the input. The tsf opcode simulates the printer being ready by setting a counter to a randomly generated number between 1 and 10 on the first call of tsf. Subsequent calls to tsf decrement the counter by 1 until 0 is reached again. On 0, the printer is ready to print, and the opcode skips to the next instruction.

A test case has been included that prints out a welcome message that asks for the users name. The user can then enter in their name (up to 8 characters) and press enter. When either 8 characters or enter has been reached, the program will print out “nice to meet you name”. All printed and stored messages take place inside of the PDP8 simulator.

GUI Debugger
The GUI debugger was implemented using gtk3. Here is a list of features that the GUI debugger has:
1. Options to step and run through the program
2. Can set and remove both breakpoints and tracepoints.
3. Button to show all breakpoints.
4. View register values once a breakpoint, tracepoint, or halt instruction has been reached when running. When stepping, register values are updated every step.
5. Ability to view any of the 32 pages of memory whenever program execution is stalled.
6. Ability to view the branch trace and memory trace results whenever the programs execution is stalled.
7. Return the memory value at a specified address.
8. Opens the list file of the object file and steps through the code in tandem with the step button.

Test Cases
Non-Micro Instructions

AND_test.as
/ Date : Feb 7, 2015
/
/ Desc : Tests the AND instruction
/ Should take 8 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,
cla cll	/ clear AC and Link
tad fillAccum	/ Fill accum with 1s
and andMask	/ Keep 731
and zero	/ Zero out accum
hlt	/ Halt the system
jmp Main	/Incase something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
fillAccum, 7777	/ All 1s
andMask, 731	/ Bitmask for the and test
zero, 0

$Main	/ End of Program; Main is entry point
----------------------------------------------------------------------------------------------------------------------------
ISZ_test.as
/ Date : Feb 7, 2015
/ 10 clock cycles since TAD is skipped
/ X = 0 and Y = 51 at the end of the program
/ Desc : Tests the ISZ instruction
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,
cll cla	/ Clear link and accum
isz X	/ Increment but don't skip
isz X	/ Increment but don't skip
isz X	/ Increment and do skip
tad Y	/ If this is executed, ISZ is wrong
isz Y	/ Increment and don't skip
hlt	/ Halt the system

/
/ Data Section
/
*0250	/ place data at address 0250
X, 7775	/ -3 decimal
Y, 50	/ 50 octal

$Main	/ End of Program; Main is entry point
----------------------------------------------------------------------------------------------------------------------------
JMP_test.as
/ Program : JMP_test.as
/ Date : Feb 11, 2015
/ Should take 8 cycles
/ 2 JMPS, 2 TADs, 2 uOps
/-------------------------------------------
/
/ Code Section
/
*0200	/ start at address 0200
Main,
cla cll	/ Clear link and accum
tad A	/ Put 2 in accum
jmp Add	/ Goto add

Halt,
hlt	/ Halt program

ADD,
tad B	/ Add 3 to accum
jmp Halt / Goto Halt
tad B	/ Should never execute this instruction
/
/ Data Section
/
*0250	/ place data at address 0250
A,	2	/ A equals 2
B,	3	/ B equals 3

$Main	/ End of Program; Main is entry point
----------------------------------------------------------------------------------------------------------------------------
JMS_DCA_test.as
/ Program : JMS_DCA_test.as
/ Date : Feb 2, 2015
/ 12 cycles in total
/ C = 5 at the end of the program and accum = 0
/-------------------------------------------
/ Code Section
/
*0200	/ start at address 0200
Main,
cla cll	/ clear AC and Link
jms Add	/ Go to sub
hlt	/ Halt program

Add,	/ C = A + B
nop	/ Space for return address
tad A	/ add A to Accumulator
tad B	/ add B
dca C	/ store sum at C
jmp i ADD	/ Return to main
/
/ Data Section
/
*0250	/ place data at address 0250
A,	2	/ A equals 2
B,	3	/ B equals 3
C,	0
$Main	/ End of Program; Main is entry point
----------------------------------------------------------------------------------------------------------------------------
TAD_test.as
/ Date : Feb 7, 2015
/ 23 cycles in total
/ 9 TAD, 5 uOps
/ Desc : Tests the TAD instruction
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,
cll cla	/ Clear link and accum
tad A	/ 0 + 5 = 5 octal
tad B	/ 5 + 10 = 15 decimal or 17 octal
tad C	/ 15 + -20 = -5 decimal or 7773 octal
cla
tad E	/ 0 + -7 = -7 decimal or 7771 octal
tad F	/ -7 + -19 = -26 or 7746 octal. Produces carry out. Compliment link
cla
tad D	/ 0 + 2047 = 2047 decimal or 3777 octal
tad A	/ 2047 + 5 = -2044 decimal or 4004 octal. No carry out. Link = 1 still
cla
tad E	/ 0 + -7 = -7 decimal or 7771 octal
tad F	/ -7 + -19 = -26 or 7746 octal. Produces carry out. Compliment link
hlt	/ Halt the system

/
/ Data Section
/
*0250	/ place data at address 0250
A, 5	/ 5 in decimal
B, 12	/ 10 in decimal
C, 7754	/ -20 in decimal
D, 3777	/ 2047 in decimal - largest positive number
E, 7771	/ -7 in decimal
F, 7755	/ -19 in decimal

$Main	/ End of Program; Main is entry point
----------------------------------------------------------------------------------------------------------------------------
Micro Instruction Tests
group_1.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 1 micro instructions
/ Should take 27 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,
cla cll	/ clear AC and Link
nop	/ no operation
dca A	/ overwrite A, should change to zero
cma cml	/ complement AC and link, should be all 1's
dca B	/ store in B, should be 1's
cla	/ clear AC, but link is still 1
rar	/ link bit rotates to bit 0 of AC
dca C	/ store in C, should be 4000 octal
cml rtr	/ set link, link bit rotates to bit 1 of AC
dca D	/ store in D, should be 2000 octal
cml ral	/ set link, link bit rotates to bit 11 of AC
dca E	/ store in E, should be 1 octal
cml rtl	/ set link, link bit rotates to bit 10 of AC
dca F	/ store in E, should be 2 octal
iac	/ increment AC
dca G	/ should be 1
cma iac	/ complement AC, then increment AC
dca H	/ should be 0
hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 7777	/ cla will change this to zero
B, 0	/ cma will change this to 1's
C, 0	/ rar will change this to 04000
D, 0	/ rtr will change this to 02000
E, 0	/ ral will change this to 01
F, 0	/ rtl will change this to 02
G, 0	/ iac will change this to 01
H, 7777	/ iac will change this to 0
----------------------------------------------------------------------------------------------------------------------------

group_2_OR_test_1.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions
/ Should take 21 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test skips working first
cla cll	/ clear AC and link
tad A	/ load AC with -1
sma	/ skip on minus AC
dca B	/ overwrite B if SMA fails, should not run
cla cll	/ clear AC and link
sza	/ skip on zero AC
dca C	/ overwrite C if SZA fails, should not run
cla cll cml	/ clear AC and link, set link high
snl	/ skip on nonzero link
dca D	/ overwrite D if SZA fails, should not run

/ Test skips failing
cla cll	/ clear AC and link
sma	/ skip on minus AC
dca E	/ overwrite E if SMA fails, should run
cla cll cma	/ clear AC and link
sza	/ skip on zero AC
dca F	/ overwrite F if SZA fails, should run
cla cll	/ clear AC and link, set link high
snl	/ skip on nonzero link
dca G	/ overwrite G if SZA fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 7777	/ -1
B, 0	/ will get -1 if sma fails
C, 1	/ will get 0 if sza fails
D, 2	/ will get 0 if snl fails
E, 3	/ will get 0 when sma fails
F, 4	/ will get 7777 when sza fails
G, 5	/ will get 0 when snl fails
----------------------------------------------------------------------------------------------------------------------------

group_2_OR_test_2.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions
/ Should take 25 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test combos of sma and sza
cla cll cma	/ clear AC and link, load AC with -1
sma	sza	/ skip on minus AC, zero AC
dca B	/ overwrite B if SMA sza fails, should not run
cla cll	/ clear AC and link
sma sza	/ skip on minus AC, zero AC
dca C	/ overwrite C if SMA SZA fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sma sza	/ skip on minus AC, zero AC
dca D	/ overwrite C if SMA SZA fails, should run

cla cll cma	/ clear AC and link, load AC with -1
sma	snl	/ skip on minus AC, non-zero link
dca E	/ overwrite E if sma snl fails, should not run
cla cll cml	/ clear AC and link, set link high
sma snl	/ skip on minus AC, non-zero link
dca F	/ overwrite F if sma snl fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sma snl	/
dca G	/ overwrite G if sma snl fails, should run

cla cll	/ clear AC and link, load AC with -1
sza	snl	/ skip on minus AC, non-zero link
dca H	/ overwrite H if sma snl fails, should not run
cla cll cml	/ clear AC and link, set link high
sza snl	/ skip on minus AC, non-zero link
dca I	/ overwrite I if sma snl fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sza snl	/
dca J	/ overwrite J if sma snl fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
B, 0	/ should not change
C, 1	/ should not change
D, 2	/ will get 1 when sma sza fails
E, 3	/ should not change
F, 4	/ should not change
G, 5	/ will get 1 when sma snl fails
H, 6	/ should not change
I, 7	/ should not change
J, 10	/ will get 1 when sza snl fails
----------------------------------------------------------------------------------------------------------------------------
group_2_OR_test_3.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions
/ Should take 25 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test combos sma sza snl at the same time
cla cll cma	/ clear AC and link, load AC with -1
sma	sza snl	/ skip on minus AC, zero AC, non-zero link
dca B	/ overwrite B if SMA sza snl fails, should not run
cla cll	/ clear AC and link
sma	sza snl	/ skip on minus AC, zero AC, non-zero link
dca C	/ overwrite C if SMA SZA snl fails, should not run
cla cll iac cml	/ clear AC and link, set AC to 1, set link to 1
sma	sza snl	/ skip on minus AC, zero AC, non-zero link
dca D	/ overwrite C if SMA SZA snl fails, should not run

cla cll iac	/ clear AC and link, load AC with 1
sma	sza snl	/ skip on minus AC, zero AC, non-zero link
dca E	/ overwrite E if sma snl fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
B, 0	/ should not change
C, 1	/ should not change
D, 2	/ should not change
E, 3	/ will get 1 when sma sza snl fails
----------------------------------------------------------------------------------------------------------------------------

group_2_AND_test_1.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions, AND subgroup
/ Should take 19 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test skips working first
cla cll iac	/ clear AC and link, set AC to 1
spa	/ skip on positive AC
dca A	/ overwrite A if spa fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sna	/ skip on non-zero AC
dca B	/ overwrite B if sna fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
szl	/ skip on zero link
dca C	/ overwrite C if szl fails, should not run

/ Test skips failing
cla cll cma	/ clear AC and link
spa	/ skip on positive AC
dca D	/ overwrite D if spa fails, should run
cla cll	/ clear AC and link
sna	/ skip on non-zero AC
dca E	/ overwrite E if sna fails, should run
cla cll cml	/ clear AC and link, set link to 1
szl	/ skip on zero link
dca F	/ overwrite F if szl fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 0	/ should not change
B, 0	/ should not change
C, 0	/ should not change
D, 77	/ will get 7777 when spa fails
E, 77	/ will get 0 when sna fails
F, 77	/ will get 0 when szl fails
----------------------------------------------------------------------------------------------------------------------------

group_2_AND_test_2.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions, AND subgroup
/ Should take 31 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test skips working first
cla cll iac	/ clear AC and link, set AC to 1
spa	sna	/ skip on positive AC, non-zero AC
dca A	/ overwrite A if spa sna fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sna	szl	/ skip on non-zero AC, zero link
dca B	/ overwrite B if sna szl fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
spa szl	/ skip on positive AC, zero link
dca C	/ overwrite C if szl fails, should not run

/ Test skips failing
cla cll cma	/ clear AC and link, load AC with 7777
spa	sna	/ skip on positive AC, non-zero AC
dca D	/ overwrite D if spa fails, should run
cla cll	/ clear AC and link
spa	sna	/ skip on positive AC, non-zero AC
dca E	/ overwrite E if spa fails, should run

cla cll	/ clear AC and link
sna	szl	/ skip on non-zero AC, zero link
dca F	/ overwrite F if sna szl fails, should run
cla cll iac cml	/ clear AC and link, set AC to 1, set link to 1
sna	szl	/ skip on non-zero AC, zero link
dca G	/ overwrite G if sna fails, should run

cla cll cml	/ clear AC and link, set link to 1
spa szl	/ skip on positive AC, skip on zero link
dca H	/ overwrite H if szl fails, should run
cla cll iac cml	/ clear AC and link, set AC to 1, set link to 1
spa szl	/ skip on positive AC, skip on zero link
dca I	/ overwrite I if szl fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 0	/ should not change
B, 0	/ should not change
C, 0	/ should not change
D, 77	/ will get 7777 when spa fails
E, 77	/ will get 0 when sna fails
F, 77	/ will get 0 when szl fails
G, 77	/ will get 1 when szl fails
H, 77	/ will get 0 when szl fails
I, 77	/ will get 1 when szl fails
----------------------------------------------------------------------------------------------------------------------------
group_2_AND_test_3.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions, AND subgroup
/ Should take 15 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test skips working first
cla cll iac	/ clear AC and link, set AC to 1
spa	sna szl	/ skip on positive AC, non-zero AC, zero link
dca A	/ overwrite A if spa sna fails, should not run

/ Test skips failing
cla cll cma	/ clear AC and link, set AC to 7777
spa	sna szl	/ skip on positive AC, non-zero AC, zero link
dca B	/ overwrite B if spa sna fails, should run

cla cll	/ clear AC and link
spa	sna szl	/ skip on positive AC, non-zero AC, zero link
dca C	/ overwrite C if spa sna fails, should run

cla cll iac cml	/ clear AC and link, set AC to 1, set link to 1
spa	sna szl	/ skip on positive AC, non-zero AC, zero link
dca D	/ overwrite D if spa sna fails, should not run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 0	/ should not change
B, 77	/ will get 7777 when sna fails
C, 77	/ will get 0 when szl fails
D, 77	/ will get 1 when spa fails
----------------------------------------------------------------------------------------------------------------------------

group_2_AND_test_4.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions, AND subgroup
/ Should take 15 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test SKP
cla cll iac	/ clear AC and link, set AC to 1
skp	/ skip
dca A	/ overwrite A if skp fails, should not run

/ Test CLA
cla cll iac	/ clear AC and link, set AC 1
sma cla	/ skip, clear AC
dca B	/ overwrite B if sma fails, should run

cla cll	/ clear AC and link
osr	/ OR switch register with AC
dca C	/ overwrite C, should run

cla cll	iac cml	/ clear AC and link, set AC to 1, set link to 1
spa cla hlt	/ skip on positive AC, clear AC
dca D	/ overwrite D if spa sna fails, should not run
dca E	/ overwrite E if spa sna fails, should not run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 0	/ should not change
B, 77	/ will get 0 when sma fails
C, 77	/ will get OCR contents
D, 77	/ should not change
E, 77	/ should not change
----------------------------------------------------------------------------------------------------------------------------
Effective_address.as
/Test case: Effective address calculation
/ Objective: test all addressing modes and
/ and the entire range of autoincrement
/ address
/
/ Description: It has a pointer before 10 and past
/ address 10 it should only out increment 10-17
/ not the others. Also access the same array using
/ zero page indirect
*7
var1,	Array
Ptr0,	Array-1
Ptr1,	Array-1
Ptr2,	Array-1
Ptr3,	Array-1
Ptr4,	Array-1
Ptr5,	Array-1
Ptr6,	Array-1
Ptr7,	Array-1
Ptr8,	Array

*50
C,	0 / C=0 to start C=6 at the end

*0200	/ start at address 0200
Main,	cla cll	/ clear AC and Link
tad i Ptr0	/ Auto inc. add Array[1] to Accumulator
tad i Ptr1	/ Auto inc. add Array[1]to Accumulator
tad i Ptr2	/ Auto inc. add Array[1] to Accumulator
tad i Ptr3	/ Auto inc. add Array[1] to Accumulator
tad i Ptr4	/ Auto inc. add Array[1] to Accumulator
tad i Ptr5	/ Auto inc. add Array[1] to Accumulator
tad i Ptr6	/ Auto inc. add Array[1] to Accumulator
tad i Ptr7	/ Auto inc. add Array[1] to Accumulator

dca A	/ Current page direct
        tad i B / current page indirect
tad i Ptr8	/ NOT Auto inc. add Array to Accumulator
tad i var1	/ Not Auto inc. add Array to Accumulator
dca C	/ Direct Zero page
hlt	/ Halt program
jmp Main	/ To continue - goto Main
/
/ Data Section
/

*0250	/ place data at address 0250
A,	0	/ A=0 at start A=20 at the end
B,	300	/ B used as address to array

/ auto incremented
*300
Array,	2
0

$Main	/ End of Program; Main is entry point
----------------------------------------------------------------------------------------------------------------------------
Effective_address2.as
/Similar the the other Effective address
/ calcualion test but on this one we are not using
/ indirect mode so address 10 -17
/ should not be incremented
*7
var1,	Array
Ptr0,	2
Ptr1,	2
Ptr2,	2
Ptr3,	2
Ptr4,	2
Ptr5,	2
Ptr6,	2
Ptr7,	2
Ptr8,	Array

*50
C,	0 / C=0 to start C=6 at the end

*0200	/ start at address 0200
Main,	cla cll	/ clear AC and Link
tad Ptr0	/ Auto inc. add Array[1] to Accumulator
tad Ptr1	/ Auto inc. add Array[1]to Accumulator
tad Ptr2	/ Auto inc. add Array[1] to Accumulator
tad Ptr3	/ Auto inc. add Array[1] to Accumulator
tad Ptr4	/ Auto inc. add Array[1] to Accumulator
tad Ptr5	/ Auto inc. add Array[1] to Accumulator
tad Ptr6	/ Auto inc. add Array[1] to Accumulator
tad Ptr7	/ Auto inc. add Array[1] to Accumulator

dca A	/ Current page direct
        tad i B / current page indirect
tad i Ptr8	/ NOT Auto inc. add Array to Accumulator
tad i var1	/ Not Auto inc. add Array to Accumulator
dca C	/ Direct Zero page
hlt	/ Halt program
jmp Main	/ To continue - goto Main
/
/ Data Section
/

*0250	/ place data at address 0250
A,	0	/ A=0 at start A=20 at the end
B,	300	/ B used as address to array

/ auto incremented
*300
Array,	2
0

$Main	/ End of Program; Main is entry point
----------------------------------------------------------------------------------------------------------------------------
IO_test.as
/ Date : Feb 13, 2015
/
/ This tests the I/O function of the PDP8
/ The program will ask for your name (up to 8 characters long).
/ It will then say "Nice to meet you name"
/
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,
cll cla
jms printGreeting	/ Greets the user and asks for name
jms getName	/ Gets name from user
jms printResponse / Prints out response plus name
hlt

printGreeting,
NOP
cla
printLoop,
tad i gPtr	/ Put next character in accumulator
poll,	tsf	/ Check printer flag
jmp poll	/ Loop until we can print
tls	/ Print the character
cla	/ Clear accumulator
isz gPtr	/ Move to the next character
isz gLen	/ Used to end loop
jmp printLoop	/ Loop until done printing greeting
jmp i printGreeting	/Return to main

getName,
NOP
cla
tad namePtr	/ Load pointer of char1 into accum
dca tempPtr	/ Make copy of the pointer
nameLoop,
ksf	/ Skip only if char inputted
jmp nameLoop
krb	/ Read in the char to accum
dca i tempPtr	/ Deposit char into memory

tad numChars	/ Put in accum
tad negOne	/ Decrement the number
dca numChars	/ Store back

tad numChars	/ Reload in accum
tad maxLen	/ Add 8 to number
spa	/ Skip if (numChars + 8) > 0
jmp i getName	/ Return to main

cla	/ Clear accum
tad i tempPtr	/ Load the inputted char
tad enterChk	/ Subtract the ascii value of enter
sna	/ Skip if (character - enter) != 0
jmp i getName	/ Return to main

cla	/ Clear accum
isz tempPtr	/ Increment char ptr
jmp nameLoop	/ Grab another char

printResponse,
NOP
cla
resLoop,
tad i oPtr	/ Put next character in accumulator
pLoop,	tsf	/ Check printer flag
jmp pLoop	/ Loop until we can print
tls	/ Print the character
cla	/ Clear accumulator
isz oPtr	/ Move to the next character
isz oLen	/ Used to end loop
jmp resLoop	/ Loop until done printing hard coded responseo

tad namePtr	/ Load in nameptr to Accum
dca tempPtr	/ Make copy of the pointer

printName,
tad i tempPtr	/ Load in name char
nLoop,	tsf	/ Check printer flag
jmp nLoop	/ Loop until printer ready
tls	/ Print the char
cla	/ Clear accum
isz tempPtr	/ Increment character address
isz numChars	/ Check to see if all chars printed
jmp printName	/ Continue printing name
jmp i printResponse	/Return to main

/
/ Data Section
/
*0300
gPtr, 0302	/ Ptr to starting address of greeting
gLen, 7745	/ -27 to print all characters in greeting
2560	/ W
3200	/ h
3020	/ a
3500	/ t
1000	/ space
3220	/ i
3460	/ s
1000	/ space
3620	/ y
3360	/ o
3520	/ u
3440	/ r
1000	/ space
3340	/ n
3020	/ a
3320	/ m
3120	/ e
1000	/ space
1200	/ (
3320	/ m
3020	/ a
3600	/ x
1000	/ space
1600	/ 8
1220	/ )
1760	/ ?
1000	/space

negOne, 7777	/ -1 Decimal
numChars, 0	/ Decrement when char entered
maxLen, 0010	/ Maximum of 8 characters allowed
namePtr, 0343	/ Ptr to char1
tempPtr, 0	/ Copy of ptr for filling letters
enterChk, 7540	/ -160 in decimal to check for enter keypress
char1, 0	/ Letter 1
char2, 0	/ Letter 2
char3, 0	/ Letter 3
char4, 0	/ Letter 4
char5, 0	/ Letter 5
char6, 0	/ Letter 6
char7, 0	/ Letter 7
char8, 0	/ Letter 8
char9, 240	/ Newline

oPtr, 0356	/Pointer for output message
oLen, 7756	/ -18 - increment to print out message
240	/ Newline
2340	/ N
3220	/ i
3060	/ c
3120	/ e
1000	/ space
3500	/ t
3360	/ o
1000	/ space
3320	/ m
3120	/ e
3120	/ e
3500	/ t
1000	/ space
3620	/ y
3360	/ o
3520	/ u
1000	/ space
$Main	/ End of Program; Main is entry point
----------------------------------------------------------------------------------------------------------------------------
OSR_test.as
/ Program : OSR_test.as
/ Date : March 5th, 2015
/
/ Desc : This program tests the OSR instruction
/ Should take 5 cycles and 4 instructions
/
/-------------------------------------------
/
/ Code Section
/
*0200	/ start at address 0200
Main,	cla cll	/ clear AC and Link
OSR	/ Grab switch register value
dca switch	/ store SR value at switch
hlt	/ Halt program
/
/ Data Section
/
*0250	/ place data at address 0250
switch,	0	/ Holds switch register value
$Main	/ End of Program; Main is entry point

Source Code

branch_trace.c
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** branch_trace.c - Implements the branch trace file functions
******************************************************************************/

#include "branch_trace.h"

/* Declare branch text types */
const char* const unconditional_text = "Unconditional";
const char* const conditional_text = "Conditional";
const char* const sub_text = "Subroutine";

/******************************************************************************
** THIS FUNCTIONS OPENS THE BRANCH TRACE FILE
******************************************************************************/
int branch_trace_init(void) {
const char* trace_name = "branch_trace.txt";
int retval = 0;
branch_file = fopen(trace_name, "w");

if(branch_file == NULL) {
#ifdef TRACE_DEBUG
printf("ERROR: Failed to open branch trace file.\n");
#endif
retval = -2;
}
else {
#ifdef TRACE_DEBUG
printf("Branch trace file opened successfully\n");
#endif
retval = 0;
}

return retval;
}

/*******************************************************************************
** THIS FUNCTION WRITES TO THE BRANCH TRACE FILE
** IT TAKES IN THE CURRENT PC, THE INSTRUCTION NAME, AND THE BRANCH TARGET
** TAKEN = 0 MEANS NOT TAKEN, TAKEN = 1 MEANS BRANCH TAKEN
******************************************************************************/
void write_branch_trace(uint16_t PC, uint16_t target_address, const char* opcode, uint8_t taken) {
char result_text[10];

if(taken) strcpy(result_text, "Taken");
else strcpy(result_text, "Not Taken");

fprintf(branch_file, "Current PC: %04o, Target: %04o, Type: %s, Result: %s\n", PC - 1,
target_address, opcode, result_text);
}

/******************************************************************************
** WRITES TO THE BRANCH TRACE FILE IN THE MIDDLE OF THE PROGRAM
******************************************************************************/
void update_branch_trace(void) {
const char* trace_name = "branch_trace.txt";

fclose(branch_file);
branch_file = fopen(trace_name, "a");

#ifdef TRACE_DEBUG
if(branch_file == NULL) {
printf("ERROR: Failed to open branch trace file for append.\n");
}
else {
printf("Branch trace file opened successfully for append\n");
}
#endif
}

int close_branch_trace(void) {
int retval;

retval = fclose(branch_file);

return retval;
}

branch_trace.h
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** branch_trace.h
******************************************************************************/

#ifndef BRANCH_TRACE_H
#define BRANCH_TRACE_H

#include <stdio.h>
#include <string.h>
#include <inttypes.h>

FILE* branch_file;

/* Branch type for branch trace file */
extern const char* const unconditional_text;
extern const char* const conditional_text;
extern const char* const sub_text;

int branch_trace_init(void);
void write_branch_trace(uint16_t, uint16_t, const char*, uint8_t);
void update_branch_trace(void);
int close_branch_trace(void);

#endif

callback.c
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** callback.c - Implements the callback functions for the buttons, radio buttons,
** and text boxes found in the GUI.
******************************************************************************/

#include "callback.h"
#include "gui.h"
#include "memory.h"
#include "main.h"

extern uint8_t tracepoint_reached;	//From memory.h
extern uint8_t tracepoint_number;	//From memory.h

/********************************************************************
        Buttons
********************************************************************/

/******************************************************************************
** CHOSES THE PAGE OF MEMORY VALUES TO PRINT OUT
******************************************************************************/
void page_number_entry_callback (GtkEntry *entry, gpointer user_data)
{
   g_items * local_object;
   const char *pagenumber_text;
const char *octal_error = "The inputted address is not a valid octal address";
const uint16_t maximum_page_num = 037;
char buffer_text[50];
static int valid_octal;
   pagenumber_text = gtk_entry_get_text(entry);
   local_object = (g_items *) user_data;

check_if_octal( atoi(pagenumber_text), &valid_octal );

local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
if(valid_octal) {
   local_object->coherance_vars->last_mem_page = strtol(pagenumber_text, NULL, 8);	//Use octal base

if(local_object->coherance_vars->last_mem_page > maximum_page_num) {
sprintf(buffer_text, "Page number %02o is out of range", local_object->coherance_vars->last_mem_page );
gtk_text_buffer_set_text (local_object->msgbuff, buffer_text, -1);
}
else {
print_memory_page(local_object->coherance_vars->last_mem_page);
update_memory_buffer(local_object);
gtk_text_buffer_set_text (local_object->msgbuff, "", -1);
}
}
else {
      gtk_text_buffer_set_text (local_object->msgbuff, octal_error, -1);
}

   // clear screen to confirm entry
    gtk_entry_set_text (entry,"\0");
}

/******************************************************************************
** LOADS A BUFFER ON THE GUI WITH TEXT FROM A TEXTFILE
******************************************************************************/
void load_buffer(g_items *object, const char* text_name, GtkTextBuffer* text_buffer)
{
    gchar *contents;
    gsize length;

    object->FP = g_file_new_for_path (text_name);

    if (g_file_load_contents (object->FP, NULL, &contents, &length, NULL, NULL))
    {
        gtk_text_buffer_set_text (text_buffer, contents, length);
        g_free (contents);
    }
    g_free (object->fname);
}

/******************************************************************************
** SHOW ALL BREAKPOINTS
******************************************************************************/
void show_breakpoints_click (GtkButton *button, gpointer data)
{
g_items* local_object = (g_items*)data;

print_breakpoints();
load_buffer(local_object, "breakpoints.txt", local_object->msgbuff);
}

/******************************************************************************
** CLOSES THE SIMULATOR AND PRINTS STATS
******************************************************************************/
void exit_button_click(GtkButton *button, gpointer data)
{
  g_items* local_object = (g_items*)data;
  shutdown_system(local_object->coherance_vars);
  gtk_widget_destroy(GTK_WIDGET(local_object->window));
}

/******************************************************************************
** RUNS UNTIL A BREAKPOINT OR TRACEPOINT IS HIT
******************************************************************************/
void run_button_click (GtkButton *button,
        gpointer data)
{
int thread1_return, thread2_return;
pthread_t keyboard_thread, simulator_thread;
   g_items* local_object = (g_items*)data;
char buffer_text[60];

//Don't do anything if execution is complete
if(local_object->coherance_vars->execution_done) goto EXECUTION_DONE;

//Tell the GUI we have ran at least once and that we intend to run, not step
local_object->coherance_vars->ran_once = 1;
local_object->coherance_vars->step_or_run = RUN;

thread1_return = pthread_create(&keyboard_thread, NULL, read_keyboard, (void*)(local_object->coherance_vars->kb_ptr));
if(thread1_return) {
fprintf(stderr, "Keyboard thread failed\n");
exit(-1);
   }

thread2_return = pthread_create( &simulator_thread, NULL, run_program, (void*)(local_object->coherance_vars));
if(thread2_return) {
fprintf(stderr, "Simulator thread failed\n");
exit(-2);
   }

//Run the threads
pthread_join(keyboard_thread, NULL);
pthread_join(simulator_thread, NULL);

//Check after thread exits
//Update the screen values
loadscreen_trace(local_object);	//update the trace window
update_labels(local_object);

//Update the text files and the buffer
print_memory_page(local_object->coherance_vars->last_mem_page);
print_memory_list();
update_memory_buffer(local_object);

if(local_object->coherance_vars->breakpoint_reached) {
local_object->coherance_vars->breakpoint_reached = 0;
local_object->coherance_vars->breakpoint_serviced = 1;

local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
sprintf(buffer_text, "Breakpoint reached at address %04o",
local_object->coherance_vars->registers_ptr->PC);
      gtk_text_buffer_set_text (local_object->msgbuff, buffer_text,-1);
}

if(tracepoint_reached) {
tracepoint_reached = 0;

local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
sprintf(buffer_text, "Tracepoint at address %04o touched by instruction at address %04o",
tracepoint_number,
local_object->coherance_vars->registers_ptr->PC - 1);
      gtk_text_buffer_set_text (local_object->msgbuff, buffer_text, -1);
}

EXECUTION_DONE:
if(local_object->coherance_vars->execution_done) {
local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
sprintf(buffer_text, "Execution of program complete");
gtk_text_buffer_set_text (local_object->msgbuff, buffer_text, -1);
update_labels(local_object);
}
}

/******************************************************************************
** EXECUTES ONE OPCODE BEFORE HALTING AGAIN
******************************************************************************/
void step_button_click(GtkButton *button, gpointer data)
{
   g_items* local_object = (g_items*)data;
char buffer_text[60];

//Tell the GUI we have ran at least once and that we intend to step
local_object->coherance_vars->ran_once = 1;
local_object->coherance_vars->step_or_run = STEP;

//Don't do anything if execution is complete
if(local_object->coherance_vars->execution_done) goto EXECUTION_DONE;

execute_opcode(local_object->coherance_vars);

//Update the screen values
loadscreen_trace(local_object);	//update the trace window
update_labels(local_object);

//Update text files and buffer
print_memory_page(local_object->coherance_vars->last_mem_page);
print_memory_list();
update_memory_buffer(local_object);

EXECUTION_DONE:
if(local_object->coherance_vars->execution_done) {
local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
sprintf(buffer_text, "Execution of program complete");
gtk_text_buffer_set_text (local_object->msgbuff, buffer_text, -1);
}
}

/******************************************************************************
** PRINT OUT THE BRANCH TRACE FILE TO TEXT WINDOW
******************************************************************************/
void loadscreen_trace(g_items* local_object) {
gchar *contents;
   gsize length;

if(local_object->coherance_vars->branch_trace) {
update_branch_trace();
local_object->FP = g_file_new_for_path ("branch_trace.txt");
}
else {
update_memory_trace();
local_object->FP = g_file_new_for_path ("memory_trace.txt");
}

if (g_file_load_contents (local_object->FP, NULL, &contents, &length, NULL, NULL))
   {
   gtk_text_buffer_set_text (local_object->trace_text_buffer, contents, length);
      g_free (contents);
   }
   g_free (local_object->fname);
}

/******************************************************************************
** PRINTS THE BRANCH TRACE FILE TO THE GUI WINDOW
******************************************************************************/
void Display_Mem_trace (GtkWidget *button, gpointer user_data)
{
    g_items* local_object = (g_items *) user_data;

    if (gtk_toggle_button_get_active (GTK_TOGGLE_BUTTON (button)))
    {
 local_object->coherance_vars->branch_trace = 0;
 loadscreen_trace(local_object);
 #ifdef GUI_DEBUG
        g_print ("\nDisplay MEM Trace!\n");
 #endif
    }

}

/******************************************************************************
** PRINTS THE BRANCH TRACE FILE TO THE GUI WINDOW
******************************************************************************/
void Diplay_branch_trace(GtkWidget *button, gpointer user_data)
{
    g_items* local_object = (g_items *) user_data;

 if (gtk_toggle_button_get_active (GTK_TOGGLE_BUTTON (button))) {
local_object->coherance_vars->branch_trace = 1;
loadscreen_trace(local_object);
#ifdef GUI_DEBUG
     g_print ("\nDisplay Branch Trace!\n");
#endif
  }
}

/******************************************************************************
** PRINTS THE LIST FILE TO THE SCREEN
******************************************************************************/
void display_lst_file(GtkWidget *button, gpointer user_data)
{
   g_items* local_object = (g_items *) user_data;

 if (gtk_toggle_button_get_active (GTK_TOGGLE_BUTTON (button))) {
        load_buffer(local_object, "MEMORY_LIST.txt", local_object->buffer);
  }
}

/******************************************************************************
** PRINTS THE PAGE NUMBER
******************************************************************************/
void display_memory_page(GtkWidget *button, gpointer user_data)
{
   g_items* local_object = (g_items *) user_data;

 if (gtk_toggle_button_get_active (GTK_TOGGLE_BUTTON (button))) {
        load_buffer(local_object, "MEMORY_PAGE.txt", local_object->buffer);
  }
}

/******************************************************************************
** CHOOSES TO UPDATE THE MEMORY PAGE FILE OR THE LIST FILE
******************************************************************************/
void update_memory_buffer(g_items* local_object) {
const char* page_file = "MEMORY_PAGE.txt";
const char* list_file = "MEMORY_LIST.txt";

 if (gtk_toggle_button_get_active (GTK_TOGGLE_BUTTON (local_object->display_lst_file))) {
   load_buffer(local_object, list_file, local_object->buffer);
}
else {
   load_buffer(local_object, page_file, local_object->buffer);
}
}

/******************************************************************************
** DETERMINES IF WE WANT TO ADD OR REMOVE A BREAKPOINT
******************************************************************************/
void breakpoint_handler(GtkEntry *entry, gpointer user_data)
{
   g_items * local_object;
   const char *breakpoint_text;
const char *octal_error = "The inputted address is not a valid octal address";
static int valid_octal;
   int breakpoint_address;
   breakpoint_text = gtk_entry_get_text(entry);
   local_object = (g_items *) user_data;

check_if_octal( atoi(breakpoint_text), &valid_octal );

if(valid_octal) {
   breakpoint_address = strtol(breakpoint_text, NULL, 8);	//Use octal base

if (gtk_toggle_button_get_active (GTK_TOGGLE_BUTTON (local_object->radio_set_BP)))
{
breakpoint_to_set(breakpoint_address, local_object);
}
else{
breakpoint_to_remove(breakpoint_address, local_object);
}
}
else {
local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
      gtk_text_buffer_set_text (local_object->msgbuff, octal_error, -1);
}

   // clear screen to confirm entry
    gtk_entry_set_text (entry,"\0");
}

/******************************************************************************
** OUTPUTS THE MEMORY VALUE AT A SPECIFIED LOCATION IN THE MESSAGE BOX
******************************************************************************/
void print_memory_location (GtkEntry *entry, gpointer user_data)
{
    const int maximum_address = 07777;	//Maximum address allowed in PDP8
    const char *memory_text;
const char *octal_error = "The inputted address is not a valid octal address";
    char buffer_text[100];
    g_items * local_object = (g_items *) user_data;
    int memory_address;
static int valid_octal;
    memory_text = gtk_entry_get_text(entry);

check_if_octal( atoi(memory_text), &valid_octal );

local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
if(valid_octal) {
memory_address = strtol(memory_text, NULL, 8);	//Use octal base
if( memory_address > maximum_address)
{
sprintf(buffer_text, "Memory address %04o is out of range", memory_address);
gtk_text_buffer_set_text (local_object->msgbuff, buffer_text, -1);
}
else
{
 sprintf(buffer_text, "The memory value at address %04o is: %04o", memory_address, (memory[memory_address] & MEMORY_MASK));
 gtk_text_buffer_set_text (local_object->msgbuff, buffer_text,-1);
}
}
else {
      gtk_text_buffer_set_text (local_object->msgbuff, octal_error, -1);
}
gtk_entry_set_text (entry,"\0");
}

/******************************************************************************
** THIS FUNCTION GETS SR VALUE FROM GUI
******************************************************************************/
void sr_entry_callback (GtkEntry *entry, gpointer user_data)
{
   const int maximum_address = 07777;	//Maximum address allowed in PDP8
   const char *sr_text;
   char buffer_text[100];
   g_items *local_object = (g_items *) user_data;
   int sr_value;
static int valid_octal;
   sr_text = gtk_entry_get_text(entry);

check_if_octal( atoi(sr_text), &valid_octal);
local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
if(valid_octal) {
sr_value = strtol(sr_text, NULL, 8);	//Use octal base

if(sr_value > maximum_address) {
sprintf(buffer_text, "SR value larger than 12 bits");
}
else {
local_object->coherance_vars->registers_ptr->SR = sr_value;
sprintf(buffer_text, "SR value entered: %04o", sr_value);
}
}
else {
sprintf(buffer_text, "Not an octal value");
}

gtk_text_buffer_set_text (local_object->msgbuff, buffer_text,-1);
 gtk_entry_set_text (entry,"\0");
}

/******************************************************************************
** THIS FUNCTION ADDS A BREAKPOINT TO MEMORY
******************************************************************************/
void breakpoint_to_set(int breakpoint_address, g_items * obj)
{
    const int maximum_address = 07777;	//Maximum address allowed in PDP8
char buffer_text[100];

    obj->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (obj->messages_txt));
    if(breakpoint_address > maximum_address)
    {
sprintf(buffer_text, "Breakpoint address %o is out of range", breakpoint_address);
      gtk_text_buffer_set_text (obj->msgbuff, buffer_text,-1);
    }
    else
    {
        set_breakpoint( (uint16_t)(breakpoint_address & 0xFFFF) );
 sprintf(buffer_text, "Breakpoint set at address %04o", breakpoint_address);
        gtk_text_buffer_set_text (obj->msgbuff, buffer_text,-1);
    }
}

/******************************************************************************
** THIS FUNCTION REMOVES A BREAKPOINT FROM MEMORY
******************************************************************************/
void breakpoint_to_remove(int breakpoint_address, g_items * obj)
{
    const int maximum_address = 07777;	//Maximum address allowed in PDP8
char buffer_text[100];

    obj->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (obj->messages_txt));
    if(breakpoint_address > maximum_address)
    {
sprintf(buffer_text, "Breakpoint address %04o is out of range", breakpoint_address);
      gtk_text_buffer_set_text (obj->msgbuff, buffer_text, -1);
    }
    else
    {
        remove_breakpoint( (uint16_t)(breakpoint_address & 0xFFFF) );
 sprintf(buffer_text, "Breakpoint removed at address %04o", breakpoint_address);
        gtk_text_buffer_set_text (obj->msgbuff, buffer_text, -1);
    }
}

/******************************************************************************
** DETERMINES IF WE WANT TO ADD OR REMOVE A TRACEPOINT
******************************************************************************/
void tracepoint_handler(GtkEntry *entry,
        gpointer data)
{
   const char *tracepoint_text;
const char *octal_error = "The inputted address is not a valid octal address";
static int valid_octal;
   g_items* local_object = (g_items*)data;
   tracepoint_text = gtk_entry_get_text(entry);

check_if_octal( atoi(tracepoint_text), &valid_octal );

if(valid_octal) {
int tracepoint_address = strtol(tracepoint_text, NULL, 8);	//Use octal base

if (gtk_toggle_button_get_active (GTK_TOGGLE_BUTTON (local_object->radioB_SetTr))) {
tracepoint_to_set(tracepoint_address, local_object);
}
else {
tracepoint_to_remove(tracepoint_address, local_object);
}
}
else {
local_object->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (local_object->messages_txt));
      gtk_text_buffer_set_text (local_object->msgbuff, octal_error, -1);
}

// clear screen to confirm entry
   gtk_entry_set_text (entry,"\0");
}

/******************************************************************************
** THIS FUNCTION ADDS A TRACEPOINT TO MEMORY
******************************************************************************/
void tracepoint_to_set(int tracepoint_address, g_items * obj)
{
    const int maximum_address = 07777;	//Maximum address allowed in PDP8
char buffer_text[100];

    obj->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (obj->messages_txt));
    if(tracepoint_address > maximum_address)
    {
sprintf(buffer_text, "Tracepoint address %o is not valid", tracepoint_address);
      gtk_text_buffer_set_text (obj->msgbuff, buffer_text, -1);
    }
    else
    {
        set_tracepoint( (uint16_t)(tracepoint_address & 0xFFFF) );
 sprintf(buffer_text, "Tracepoint set at address %04o", tracepoint_address);
        gtk_text_buffer_set_text (obj->msgbuff, buffer_text, -1);
    }
}

/******************************************************************************
** THIS FUNCTION REMOVES A TRACEPOINT FROM MEMORY
******************************************************************************/
void tracepoint_to_remove(int tracepoint_address, g_items * obj)
{
    const int maximum_address = 07777;	//Maximum address allowed in PDP8
char buffer_text[100];

    obj->msgbuff = gtk_text_view_get_buffer (GTK_TEXT_VIEW (obj->messages_txt));
    if(tracepoint_address > maximum_address)
    {
sprintf(buffer_text, "Not a valid address");
      gtk_text_buffer_set_text (obj->msgbuff, buffer_text, -1);
    }
    else
    {
        remove_tracepoint( (uint16_t)(tracepoint_address & 0xFFFF) );
sprintf(buffer_text, "Tracepoint removed at address %04o", tracepoint_address);
        gtk_text_buffer_set_text (obj->msgbuff, buffer_text, -1);
    }
}

/******************************************************************************
** CHECKS TO SEE IF THE INPUTTED VALUE FROM THE USER IS VALID OCTAL VALUE
** RETURNS 1 IF INPUT IS A VALID OCTAL VALUE
** RETURNS 0 IF INPUT IS NOT A VALID OCTAL VALUE
******************************************************************************/
void check_if_octal(int input, int* value_good) {
int tens_place = input / 10;	//Checks if number is less than 10
int mod_value = input % 10;

 if ( (tens_place == 0) && (mod_value < 8) ) { // less than 10 and valid octal
    *value_good = 1;
   }
  else if(mod_value > 7) { //Not a valid octal value
    *value_good = 0;
   }
   else if (tens_place > 0) {
   check_if_octal(tens_place, value_good);
  }
}

callback.h
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** callback.h
******************************************************************************/

#ifndef _CALLBACK_H_
#define _CALLBACK_H_

#include "gui.h"

/******************************************************************* *
        PROTOTYPES Buttons
********************************************************************/
void load_buffer(g_items*, const char*, GtkTextBuffer*);

void page_number_entry_callback (GtkEntry *entry, gpointer user_data);
void run_button_click (GtkButton *button1, gpointer data);
void step_button_click(GtkButton *button, gpointer data);
void exit_button_click(GtkButton *button, gpointer data);
void show_breakpoints_click(GtkButton *button, gpointer data);
void print_memory_location (GtkEntry *entry, gpointer user_data);
void loadscreen_trace(g_items*);

//Tracepoint and breakpoint functions
void breakpoint_handler(GtkEntry *entry, gpointer user_data);
void tracepoint_handler(GtkEntry *entry, gpointer user_data);
void breakpoint_to_set(int breakpoint_address, g_items * obj);
void breakpoint_to_remove(int breakpoint_address, g_items * obj);
void tracepoint_to_set(int, g_items*);
void tracepoint_to_remove(int, g_items*);
void sr_entry_callback (GtkEntry *entry, gpointer user_data);
void display_memory_page(GtkWidget *button, gpointer user_data);
void display_lst_file(GtkWidget *button, gpointer user_data);
void update_memory_buffer(g_items*);

//Intermediate functions
void Diplay_branch_trace(GtkWidget *button, gpointer user_data);
void Display_Mem_trace (GtkWidget *button, gpointer user_data);
void check_if_octal(int, int*);

#endif
----------------------------------------------------------------------------------------------------------------------------

cpu.c
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** cpu.c - Implements the cpu opcode functions
******************************************************************************/

#include "cpu.h"
#include "memory.h"
#include "branch_trace.h"

/******************************************************************************
** OPCODE 0 - AND
******************************************************************************/
void AND(regs* registers) {
registers->MB = mem_read(registers->CPMA, DATA_READ);
registers->AC &= registers->MB;
}

/******************************************************************************
** OPCODE 1 - TAD
******************************************************************************/
void TAD(regs* registers) {
const uint16_t carry_out = 0x1000;	/* Check bit 13 for carry out */
registers->MB = mem_read(registers->CPMA, DATA_READ);
registers->AC += registers->MB;

//Keep only the first bit after complimenting
if(registers->AC & carry_out) registers->link_bit = (~registers->link_bit) & 1;

registers->AC &= CUTOFF_MASK;
}

/******************************************************************************
** OPCODE 2 - ISZ
******************************************************************************/
void ISZ(regs* registers) {
uint8_t taken = 0;
uint16_t current_PC = registers->PC;

registers->MB = mem_read(registers->CPMA, DATA_READ);
registers->MB = (registers->MB + 1) & CUTOFF_MASK;
mem_write(registers->CPMA, registers->MB);

if(!registers->MB) {
registers->PC++;
taken = 1;
}

write_branch_trace(current_PC, current_PC + 1, conditional_text, taken);
}

/******************************************************************************
** OPCODE 3 - DCA
******************************************************************************/
void DCA(regs* registers) {
registers->MB = registers->AC;
mem_write(registers->CPMA, registers->MB);
registers->AC = 0;
}

/******************************************************************************
** OPCODE 4 - JMS
******************************************************************************/
void JMS(regs* registers) {
uint8_t taken = 1;
uint16_t current_PC = registers->PC;

registers->MB = registers->PC;
mem_write(registers->CPMA, registers->MB);
registers->PC = (registers->CPMA + 1) & CUTOFF_MASK; //Start 1 address into sub

write_branch_trace(current_PC, registers->PC, sub_text, taken);
}

/******************************************************************************
** OPCODE 5 - JMP
******************************************************************************/
void JMP(regs* registers) {
uint8_t taken = 1;
uint16_t current_PC = registers->PC;

registers->PC = registers->CPMA;

write_branch_trace(current_PC, registers->PC, unconditional_text, taken);
}

/******************************************************************************
** OPCODE 6 - Keyboard - KCF
******************************************************************************/
void KCF(struct keyboard* kb_state) {
pthread_mutex_lock(&keyboard_mux);
kb_state->input_flag = 0;
pthread_mutex_unlock(&keyboard_mux);
}

/******************************************************************************
** OPCODE 6 - Keyboard - KSF
******************************************************************************/
void KSF(regs* registers, struct keyboard* kb_state) {
uint8_t taken = 0;
uint16_t current_PC = registers->PC;

pthread_mutex_lock(&keyboard_mux);
if(kb_state->input_flag) {
registers->PC++;
taken = 1;
}
pthread_mutex_unlock(&keyboard_mux);
write_branch_trace(current_PC, current_PC + 1, conditional_text, taken);
}

/******************************************************************************
** OPCODE 6 - Keyboard - KCC
******************************************************************************/
void KCC(regs* registers, struct keyboard* kb_state) {
CLA(registers);
pthread_mutex_lock(&keyboard_mux);
kb_state->input_flag = 0;
pthread_mutex_unlock(&keyboard_mux);
}

/******************************************************************************
** OPCODE 6 - Keyboard - KRS
******************************************************************************/
void KRS(regs* registers, struct keyboard* kb_state) {
pthread_mutex_lock(&keyboard_mux);
registers->AC |= kb_state->input_char << 4;
pthread_mutex_unlock(&keyboard_mux);
}

/******************************************************************************
** OPCODE 6 - Keyboard - KRB
******************************************************************************/
void KRB(regs* registers, struct keyboard* kb_state) {
registers->AC = 0;
pthread_mutex_lock(&keyboard_mux);
kb_state->input_flag = 0;
if(kb_state->input_char != '~') registers->AC |= kb_state->input_char << 4;
pthread_mutex_unlock(&keyboard_mux);
}

/******************************************************************************
** OPCODE 6 - Monitor - TFL
******************************************************************************/
void TFL(regs* registers) {
registers->print_flag = 1;
}

/******************************************************************************
** OPCODE 6 - Monitor - TSF
******************************************************************************/
void TSF(regs* registers) {
uint8_t taken = 0;
uint16_t current_PC = registers->PC;
static int printer_counter = 0;	//Initalize at 0 only

//If printer counter is 0, then choose random number
//for it to countdown to 0 with. When 0 is reached, then
//the printer flag is "set"
if(!printer_counter) {
printer_counter = (rand() % 10) + 1; //1 to 10
}
else {
printer_counter--;
if(!printer_counter) {
registers->PC++;
taken = 1;
write_branch_trace(current_PC, current_PC + 1, conditional_text, taken);
}
}
}

/******************************************************************************
** OPCODE 6 - Monitor - TCF
******************************************************************************/
void TCF(regs* registers) {
registers->print_flag = 0;
}

/******************************************************************************
** OPCODE 6 - Monitor - TPC
******************************************************************************/
void TPC(regs* registers) {
char to_print = (registers->AC >> 4) & 0xFF;
printf("%c", to_print);
fflush(stdout);
}

/******************************************************************************
** OPCODE 6 - Monitor - TLS
******************************************************************************/
void TLS(regs* registers) {
registers->print_flag = 0;
char to_print = (registers->AC >> 4) & 0xFF;
printf("%c", to_print);
fflush(stdout);
}

/******************************************************************************
** OPCODE 7 GROUP 1 - CLA
******************************************************************************/
void CLA(regs* registers) {
registers->AC = 0;
}

/******************************************************************************
** OPCODE 7 GROUP 1 - CLL
******************************************************************************/
void CLL(regs* registers) {
registers->link_bit = 0;
}

/******************************************************************************
** OPCODE 7 GROUP 1 - CMA
******************************************************************************/
void CMA(regs* registers) {
registers->AC = ~registers->AC & CUTOFF_MASK;
}

/******************************************************************************
** OPCODE 7 GROUP 1 - CML
******************************************************************************/
void CML(regs* registers) {
registers->link_bit = ~registers->link_bit & 1;
}

/******************************************************************************
** OPCODE 7 GROUP 1 - IAC
******************************************************************************/
void IAC(regs* registers) {
registers->AC = (registers->AC + 1) & CUTOFF_MASK;
}

/******************************************************************************
** OPCODE 7 GROUP 1 - RAR
******************************************************************************/
void RAR(regs* registers) {
const uint8_t bit11_shift = 11;
uint8_t old_link = registers->link_bit;

/* Shift right 1. New link is bit 0 of registers->AC.
** Bit 11 of new registers->AC is old link bit value.
*/
registers->AC >>= 1;
registers->link_bit = registers->AC & 1;
registers->AC = (registers->AC | (old_link << bit11_shift)) & CUTOFF_MASK;
}

/******************************************************************************
** OPCODE 7 GROUP 1 - RTR
******************************************************************************/
void RTR(regs* registers) {
/* Same as two RAR in a row */
RAR(registers);
RAR(registers);
}

/******************************************************************************
** OPCODE 7 GROUP 1 - RAL
******************************************************************************/
void RAL(regs* registers) {
const uint8_t shift_num = 12;	/* Shift bit 12 into bit 0 */
const uint16_t new_link_pos = 0x1000;	/* Bit 12 */

/* Shift registers->AC left 1. New link is bit 12
** Bit 0 of registers->AC is old link bit
*/
registers->AC <<= 1;
registers->AC |= registers->link_bit;
registers->link_bit = (registers->AC & new_link_pos) >> shift_num;
registers->AC &= CUTOFF_MASK;
}

/******************************************************************************
** OPCODE 7 GROUP 1 - RTL
******************************************************************************/
void RTL(regs* registers) {
/* Same as two RAL in a row */
RAL(registers);
RAL(registers);
}

/******************************************************************************
** OPCODE 7 GROUP 2 - SMA
******************************************************************************/
uint8_t SMA(regs* registers) {
const uint16_t sign_bit = 0x800;
uint8_t retval = 0;

if(registers->AC & sign_bit) {
retval = 1;
}
return retval;
}

/******************************************************************************
** OPCODE 7 GROUP 2 - SZA
******************************************************************************/
uint8_t SZA(regs* registers) {
uint8_t retval = 0;

if(!registers->AC) {
retval = 1;
}
return retval;
}

/******************************************************************************
** OPCODE 7 GROUP 2 - SNL
******************************************************************************/
uint8_t SNL(regs* registers) {
uint8_t retval = 0;

if(registers->link_bit) {
retval = 1;
}
return retval;
}

/******************************************************************************
** OPCODE 7 GROUP 2 - SPA
******************************************************************************/
uint8_t SPA(regs* registers) {
const uint16_t sign_bit = 0x800;
uint8_t retval = 0;

if( !(registers->AC & sign_bit) ) {
retval = 1;
}
return retval;
}

/******************************************************************************
** OPCODE 7 GROUP 2 - SNA
******************************************************************************/
uint8_t SNA(regs* registers) {
uint8_t retval = 0;

if(registers->AC) {
retval = 1;
}
return retval;
}

/******************************************************************************
** OPCODE 7 GROUP 2 - SZL
******************************************************************************/
uint8_t SZL(regs* registers) {
uint8_t retval = 0;

if(!registers->link_bit) {
retval = 1;
}
return retval;
}

/******************************************************************************
** OPCODE 7 GROUP 2 - SKP
******************************************************************************/
void SKP(regs* registers) {
uint8_t taken = 1;

write_branch_trace(registers->PC, registers->PC + 1, unconditional_text, taken);
registers->PC++;
}

/******************************************************************************
** OPCODE 7 GROUP 2 - OSR
******************************************************************************/
void OSR(regs* registers) {
registers->AC = (registers->AC | registers->SR) & CUTOFF_MASK;
}

/******************************************************************************
** OPCODE 7 GROUP 2 - HLT
******************************************************************************/
void HLT(struct keyboard* kb_state) {
printf("\n\nHALTING SYSTEM\n");

pthread_mutex_lock(&keyboard_mux);
kb_state->quit = 1;
pthread_mutex_unlock(&keyboard_mux);
}

/******************************************************************************
** RESET REGISTER VALUES
******************************************************************************/
void reset_regs(regs* registers) {
registers->PC = STARTING_ADDRESS;
registers->AC = 0;
registers->MQ = 0;
registers->link_bit = 0;
registers->CPMA = 0;
registers->MB = 0;
registers->SR = 0;
registers->IR = 0;
registers->print_flag = 0;
}

cpu.h
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** cpu.h
******************************************************************************/

#ifndef CPU_H
#define CPU_H

#include <stdio.h>
#include <inttypes.h>
#include <assert.h>
#include <stdlib.h>
#include <time.h>
#include "kb_input.h"

#define CUTOFF_MASK 0xFFF	/* Bitmask to keep registers/memory at 12 bits */
#define STARTING_ADDRESS 0200	// start at 200 octal

#define OP_CODE_AND	0
#define OP_CODE_TAD	01000
#define OP_CODE_ISZ	02000
#define OP_CODE_DCA	03000
#define OP_CODE_JMS	04000
#define OP_CODE_JMP	05000
#define OP_CODE_IO	06000
#define OP_CODE_MICRO	07000

#define IO_OPCODE_BITS_MASK 0077
#define MICRO_INSTRUCTION_GROUP_BIT 0400
#define MICRO_INSTRUCTION_BITS_MASK 0377
#define MICRO_GROUP2_SUBGROUP_BIT 00010

// I/O Keyboard
#define IO_OPCODE_KCF_BITS 0030
#define IO_OPCODE_KSF_BITS 0031
#define IO_OPCODE_KCC_BITS 0032
#define IO_OPCODE_KRS_BITS 0034
#define IO_OPCODE_KRB_BITS 0036

// I/O Monitor
#define IO_OPCODE_TFL_BITS 0040
#define IO_OPCODE_TSF_BITS 0041
#define IO_OPCODE_TCF_BITS 0042
#define IO_OPCODE_TPC_BITS 0044
#define IO_OPCODE_TLS_BITS 0046

// Group 1 micro instructions
#define MICRO_INSTRUCTION_CLA_BITS	0200
#define MICRO_INSTRUCTION_CLL_BITS	0100
#define MICRO_INSTRUCTION_CMA_BITS	0040
#define MICRO_INSTRUCTION_CML_BITS	0020
#define MICRO_INSTRUCTION_IAC_BITS	0001
#define MICRO_INSTRUCTION_RAR_BITS	0010
#define MICRO_INSTRUCTION_RTR_BITS	0012
#define MICRO_INSTRUCTION_RAL_BITS	0004
#define MICRO_INSTRUCTION_RTL_BITS	0006

// Group 2 micro instructions
#define MICRO_INSTRUCTION_SMA_BITS	0100
#define MICRO_INSTRUCTION_SZA_BITS	0040
#define MICRO_INSTRUCTION_SNL_BITS	0020
#define MICRO_INSTRUCTION_SPA_BITS	0110
#define MICRO_INSTRUCTION_SNA_BITS	0050
#define MICRO_INSTRUCTION_SZL_BITS	0030
#define MICRO_INSTRUCTION_SKP_BITS	0010
#define MICRO_INSTRUCTION_CLA_BITS	0200
#define MICRO_INSTRUCTION_OSR_BITS	0004
#define MICRO_INSTRUCTION_HLT_BITS	0002

/* CPU registers - only 12 bits are used of the 16 */
typedef struct {
uint16_t AC;	/* Accumulator */
uint16_t MQ;	/* Multiplier Quotient */
uint16_t PC;	/* Program Counter */
uint16_t MB;	/* Memory Buffer */
uint16_t CPMA;	/* Central Processor Memory Address */
uint16_t SR;	/* Console Switch Register */
uint8_t IR;	/* Instruction Register - only 3 bits are used */
uint8_t link_bit;	/* Carry out bit */
uint8_t print_flag;
} regs;

/* Opcodes 0-5 - Memory reference functions */
void AND(regs*);
void TAD(regs*);
void ISZ(regs*);
void DCA(regs*);
void JMS(regs*);
void JMP(regs*);

/* Opcode 6 - I/O - Keyboard */
void KCF(struct keyboard*);
void KSF(regs*, struct keyboard*);
void KCC(regs*, struct keyboard*);
void KRS(regs*, struct keyboard*);
void KRB(regs*, struct keyboard*);

/* Opcode 6 - I/O - Monitor */
void TFL(regs*);
void TSF(regs*);
void TCF(regs*);
void TPC(regs*);
void TLS(regs*);

/* Opcode 7 - group 1 */
void CLA(regs*);
void CLL(regs*);
void CMA(regs*);
void CML(regs*);
void IAC(regs*);
void RAR(regs*);
void RTR(regs*);
void RAL(regs*);
void RTL(regs*);

/* Opcoderegs* 7 - group 2 */
uint8_t SMA(regs*);
uint8_t SZA(regs*);
uint8_t SNL(regs*);
uint8_t SPA(regs*);
uint8_t SNA(regs*);
uint8_t SZL(regs*);
void SKP(regs*);
void OSR(regs*);
void HLT(struct keyboard*);

/* Reset the registers */
void reset_regs(regs*);

#endif

gui.c
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** gui.c - Implements functions that add content to the GUI window
******************************************************************************/

#include "gui.h"
#include "callback.h"
#include "main.h"

/*Create a label and set its alignment. Setting the line wrap to TRUE makes
the label break lines if the text exceeds the widget's size. When set to
FALSE the text gets cut off by the edge of the widget*/
void create_labels(g_items * obj)
{
    obj->pagenum= gtk_label_new ("Select a Page Number");
    obj->label = gtk_label_new ("Register");
    obj->PC_label= gtk_label_new ("PC");
    obj->Accumulator_label= gtk_label_new ("AC");
    obj->CPMA_label= gtk_label_new ("CPMA");
    obj->IR_label= gtk_label_new ("IR");
    obj->Link_label= gtk_label_new ("Link");
    obj->Memory_Buffer_label= gtk_label_new ("Memory Buffer");
    obj->memory_entry_label= gtk_label_new ("Memory Value At Address");
    obj->Mesages_label= gtk_label_new ("Messages");
    obj->SR_label=gtk_label_new ("SR");

    gtk_label_set_justify (GTK_LABEL (obj->pagenum), GTK_JUSTIFY_CENTER);
    gtk_label_set_justify (GTK_LABEL (obj->label), GTK_JUSTIFY_LEFT);
    gtk_label_set_justify (GTK_LABEL (obj->PC_label), GTK_JUSTIFY_LEFT);
    gtk_label_set_justify (GTK_LABEL (obj->Accumulator_label), GTK_JUSTIFY_LEFT);
    gtk_label_set_justify (GTK_LABEL (obj->CPMA_label), GTK_JUSTIFY_LEFT);
    gtk_label_set_justify (GTK_LABEL (obj->Mesages_label), GTK_JUSTIFY_CENTER);
    gtk_label_set_justify (GTK_LABEL (obj->Mesages_label), GTK_JUSTIFY_LEFT);
    gtk_label_set_justify (GTK_LABEL (obj->SR_label), GTK_JUSTIFY_LEFT);

// values

    obj->value = gtk_label_new ("Contents");
    obj->PC_value= gtk_label_new ("0");
    obj->Accumulator_value= gtk_label_new ("0");
    obj->CPMA_value = gtk_label_new ("0");
    obj->IR_value= gtk_label_new ("0");
    obj->Link_value= gtk_label_new ("0");
    obj->Memory_Buffer_value= gtk_label_new ("0");

    gtk_label_set_justify (GTK_LABEL (obj->value), GTK_JUSTIFY_LEFT);
    gtk_label_set_justify (GTK_LABEL (obj->PC_value), GTK_JUSTIFY_RIGHT);
    gtk_label_set_justify (GTK_LABEL (obj->Accumulator_value), GTK_JUSTIFY_LEFT);
    gtk_label_set_justify (GTK_LABEL (obj->CPMA_value), GTK_JUSTIFY_RIGHT);
}
/****************************************************************************
        create buttons
****************************************************************************/
void create_buttons(g_items* obj)
{
// radio button needs to be created and label created

    obj->run_button = gtk_button_new_with_label ("RUN");
    obj->show_breakpoints = gtk_button_new_with_label ("Show Breakpoints");
    obj->exit_button = gtk_button_new_with_label ("Exit");
    obj->step = gtk_button_new_with_label ("Step");
}

/****************************************************************************
        entry box
****************************************************************************/
void create_entrybox (g_items* obj)
{
    obj->BreakP_entry = gtk_entry_new();
    obj->Trace_entry = gtk_entry_new();
    obj->memory_entry= gtk_entry_new();
    obj->SR_entry= gtk_entry_new();
    obj->page_number_entry= gtk_entry_new();

}

/********************************************************************
  Create a grid and attach the button
********************************************************************/
void set_grid(g_items * obj)
{
    int lcol ,c1row, c2row;
    lcol =3;
    c1row = c2row = 2;

    obj->grid = gtk_grid_new ();
    gtk_grid_set_column_spacing (GTK_GRID (obj->grid), 10);
    gtk_grid_set_row_spacing (GTK_GRID (obj->grid), 3);
    gtk_grid_set_column_homogeneous (GTK_GRID (obj->grid), TRUE);

    //**************************************************(left ,Top, width, height)
    gtk_widget_set_vexpand (obj->scrolled_window, TRUE);
    //gtk_grid_attach (GTK_GRID (obj->grid), obj->scrolled_window ,1, 4, 2, 5);

    /* set button location on the grid */
    gtk_grid_attach (GTK_GRID (obj->grid), obj->run_button ,1, 1, 1, 1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->step, obj->run_button,GTK_POS_RIGHT,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->show_breakpoints, obj->step,GTK_POS_RIGHT,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->exit_button, obj->show_breakpoints,GTK_POS_RIGHT,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->pagenum, obj->step,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->page_number_entry, obj->pagenum,GTK_POS_BOTTOM,1,1);
    // radio button at top of the screen
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->display_memory_page, obj->page_number_entry,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->display_lst_file, obj->display_memory_page ,GTK_POS_LEFT,1,1);
    // place top text screen
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->scrolled_window, obj->display_lst_file ,GTK_POS_BOTTOM,2,5);

    /****************************************************************************
    NOTE: variables lcol and c1row are uto incremented to ensure that
    adding new things to the grid will be the one next to ot the on e
    below it
    *****************************************************************************/

//***********************************************************(left ,Top, width, height)
    gtk_grid_attach (GTK_GRID (obj->grid), obj->label , lcol , c1row , 1, 1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->PC_label, obj->label,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->Accumulator_label, obj->PC_label,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->CPMA_label, obj->Accumulator_label,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->IR_label, obj->CPMA_label,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->Link_label, obj->IR_label,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->Memory_Buffer_label, obj->Link_label,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->SR_label, obj->Memory_Buffer_label,GTK_POS_BOTTOM,1,1);

//*IR_label *Link_label, Memory_Buffer_label

    gtk_grid_attach (GTK_GRID (obj->grid), obj->value ,(++lcol), c2row , 1, 1);
    gtk_grid_attach (GTK_GRID (obj->grid), obj->PC_value, (lcol), ++c2row , 1, 1);
    gtk_grid_attach (GTK_GRID (obj->grid), obj->Accumulator_value ,lcol, ++c2row , 1, 1);
    gtk_grid_attach (GTK_GRID (obj->grid), obj->CPMA_value ,lcol, ++c2row, 1, 1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->IR_value, obj->CPMA_value,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->Link_value, obj->IR_value,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->Memory_Buffer_value, obj->Link_value,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->SR_entry, obj->Memory_Buffer_value,GTK_POS_BOTTOM,1,1);

// radio Buttons placement
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->radio_set_BP, obj->SR_entry,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->radio_clear_BP, obj->radio_set_BP,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->BreakP_entry,obj->radio_clear_BP, GTK_POS_BOTTOM, 1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->memory_entry,obj->BreakP_entry, GTK_POS_BOTTOM, 1,1);

    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->memory_entry_label, obj->memory_entry ,GTK_POS_LEFT,1,1);
    // set and clear trace points
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->radioB_SetTr, obj->SR_label,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->radioB_ClrTr, obj->radioB_SetTr,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->Trace_entry, obj->radioB_ClrTr,GTK_POS_BOTTOM,1,1);

// buttons at the buttom of text window
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->memory_trace,obj->scrolled_window ,GTK_POS_BOTTOM,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->branch_trace,obj->memory_trace ,GTK_POS_RIGHT,1,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->trace_text_window, obj->memory_trace,GTK_POS_BOTTOM,2,10);

// message window
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->Mesages_label, obj->memory_entry_label ,GTK_POS_BOTTOM,2,1);
    gtk_grid_attach_next_to (GTK_GRID (obj->grid),obj->scrolled_msg, obj->Mesages_label,GTK_POS_BOTTOM,2,1);
}

void create_buffers(g_items * obj)
{
    /* text view windows with buffers
      does not add scroll functionality here
     that is done in create_test_boxes */

    /*****************************************************************
        Text view is a widget in which can display the text buffer.
        The line wrapping is set to break lines in between words.
    *******************************************************************/
    /* The text buffer represents the text being edited */
    obj->buffer = gtk_text_buffer_new (NULL); //input buffer
    obj->text_view = gtk_text_view_new_with_buffer (obj->buffer);
    gtk_text_view_set_wrap_mode (GTK_TEXT_VIEW (obj->text_view), GTK_WRAP_WORD);

    obj->msgbuff = gtk_text_buffer_new (NULL); //input buffer
    obj->messages_txt = gtk_text_view_new_with_buffer (obj->msgbuff);
    gtk_text_view_set_wrap_mode (GTK_TEXT_VIEW (obj->messages_txt), GTK_WRAP_WORD);

    obj->trace_text_buffer = gtk_text_buffer_new (NULL); //input buffer
    obj->trace_text_view = gtk_text_view_new_with_buffer (obj->trace_text_buffer);
    gtk_text_view_set_wrap_mode (GTK_TEXT_VIEW (obj->trace_text_view), GTK_WRAP_WORD);
}

void create_text_boxes (g_items * obj)
{
    /* Create the scrolled window. Usually NULL is passed for both parameters so
     * that it creates the horizontal/vertical adjustments automatically. Setting
     * the scrollbar policy to automatic allows the scrollbars to only show up
     * when needed.
     */
    obj->scrolled_window = gtk_scrolled_window_new (NULL, NULL);
    gtk_scrolled_window_set_policy (GTK_SCROLLED_WINDOW (obj->scrolled_window),
        GTK_POLICY_AUTOMATIC,
        GTK_POLICY_AUTOMATIC);

    /* The function directly below is used to add children to the scrolled window
     * with scrolling capabilities (e.g text_view), otherwise,
     * gtk_scrolled_window_add_with_viewport() would have been used
     */
    gtk_container_add (GTK_CONTAINER (obj->scrolled_window), obj->text_view);
    gtk_container_set_border_width (GTK_CONTAINER (obj->scrolled_window), 5);

// here sets messages box

    obj->scrolled_msg = gtk_scrolled_window_new (NULL, NULL);
    gtk_scrolled_window_set_policy (GTK_SCROLLED_WINDOW (obj->scrolled_msg),
        GTK_POLICY_AUTOMATIC,
        GTK_POLICY_AUTOMATIC);

    gtk_container_add (GTK_CONTAINER (obj->scrolled_msg), obj->messages_txt);
    gtk_container_set_border_width (GTK_CONTAINER (obj->scrolled_msg), 5);

   // here set trace memory and branch trace memory text window
    obj->trace_text_window = gtk_scrolled_window_new (NULL, NULL);
    gtk_scrolled_window_set_policy (GTK_SCROLLED_WINDOW (obj->trace_text_window),
        GTK_POLICY_AUTOMATIC,
        GTK_POLICY_AUTOMATIC);

    gtk_container_add (GTK_CONTAINER (obj->trace_text_window), obj->trace_text_view);
    gtk_container_set_border_width (GTK_CONTAINER (obj->trace_text_window), 5);

}

/*****************************************************************
        CREATE RADIO BUTTONS
*******************************************************************/
void create_radio_buttons(g_items* obj)
{
    obj->radio_set_BP=gtk_radio_button_new_with_label(NULL, "Set Breakpoint");

    obj->radio_clear_BP=gtk_radio_button_new_with_label_from_widget
        (GTK_RADIO_BUTTON (obj->radio_set_BP), "Clear Breakpoint");

    obj->radioB_SetTr =gtk_radio_button_new_with_label(NULL, "Set Tracepoint");
    obj->radioB_ClrTr =gtk_radio_button_new_with_label_from_widget(
        GTK_RADIO_BUTTON (obj->radioB_SetTr), "Clear Tracepoint");

    obj->memory_trace =gtk_radio_button_new_with_label(NULL, "Memory Trace");
    obj->branch_trace =gtk_radio_button_new_with_label_from_widget(
        GTK_RADIO_BUTTON (obj->memory_trace), "Branch Trace");

    obj->display_memory_page = gtk_radio_button_new_with_label(NULL, "Display Memory Page");
    obj->display_lst_file = gtk_radio_button_new_with_label_from_widget(
        GTK_RADIO_BUTTON (obj->display_memory_page), "Display List File");
}

/*****************************************************************
        SET VALUES OF THE RADIO BUTTONS
*******************************************************************/
void set_radio_buttons( g_items *obj)
{
// set values
    gtk_toggle_button_set_active (GTK_TOGGLE_BUTTON (obj->radio_set_BP), TRUE);
    gtk_toggle_button_set_active (GTK_TOGGLE_BUTTON (obj->radio_clear_BP), FALSE);

    gtk_toggle_button_set_active (GTK_TOGGLE_BUTTON (obj->radioB_SetTr), TRUE);
    gtk_toggle_button_set_active (GTK_TOGGLE_BUTTON (obj->radioB_ClrTr), FALSE);

    gtk_toggle_button_set_active (GTK_TOGGLE_BUTTON (obj->memory_trace), TRUE);
    gtk_toggle_button_set_active (GTK_TOGGLE_BUTTON (obj->branch_trace), TRUE);

     gtk_toggle_button_set_active (GTK_TOGGLE_BUTTON (obj->display_lst_file), TRUE);
     gtk_toggle_button_set_active (GTK_TOGGLE_BUTTON (obj->display_memory_page), FALSE);
}

/*****************************************************************
        Create entry box callbacks
*******************************************************************/
void entry_box_cb(g_items *obj)
{
    g_signal_connect (GTK_ENTRY (obj->BreakP_entry), "activate",
        G_CALLBACK (breakpoint_handler), obj);

    g_signal_connect (GTK_ENTRY (obj->Trace_entry), "activate",
        G_CALLBACK (tracepoint_handler), obj);

     g_signal_connect (GTK_ENTRY (obj->memory_entry), "activate",
        G_CALLBACK (print_memory_location), obj);

    g_signal_connect (GTK_ENTRY (obj->SR_entry), "activate",
        G_CALLBACK (sr_entry_callback), obj);

 g_signal_connect (GTK_ENTRY (obj->page_number_entry), "activate",
        G_CALLBACK (page_number_entry_callback), obj);
}

/*****************************************************************
        RADIO BUTTONS CALLBACKS
*******************************************************************/
void radio_button_callbacks( g_items * obj)
{
  // trace points
   g_signal_connect (GTK_TOGGLE_BUTTON (obj->memory_trace), "toggled",
        G_CALLBACK (Display_Mem_trace), obj);

    g_signal_connect (GTK_TOGGLE_BUTTON (obj->branch_trace), "toggled",
        G_CALLBACK (Diplay_branch_trace), obj);

   g_signal_connect (GTK_TOGGLE_BUTTON (obj->display_lst_file), "toggled",
        G_CALLBACK (display_lst_file), obj);

    g_signal_connect (GTK_TOGGLE_BUTTON (obj->display_memory_page), "toggled",
        G_CALLBACK (display_memory_page), obj);
}

/*****************************************************************
        CREATE BUTTONS CALL BACK
*******************************************************************/
void create_buttons_callbacks(g_items* obj)
{
    /*Connecting the clicked signal to the callback function*/

    g_signal_connect (GTK_BUTTON (obj->run_button), "clicked",
        G_CALLBACK (run_button_click), obj);

    g_signal_connect (GTK_BUTTON (obj->step), "clicked",
        G_CALLBACK (step_button_click), obj);

    g_signal_connect (GTK_BUTTON (obj->show_breakpoints), "clicked",
        G_CALLBACK (show_breakpoints_click), obj);

    g_signal_connect (GTK_BUTTON (obj->exit_button), "clicked",
        G_CALLBACK (exit_button_click), obj);
}

void activate (GtkApplication *app, gpointer data)
{
    g_items * obj;
    obj = (g_items *) data;

    /******************************************************************
        create window and set size
    ******************************************************************/
    obj->window = gtk_application_window_new (app);
    gtk_window_set_default_size (GTK_WINDOW (obj->window), 900, 800);
    gtk_window_set_title (GTK_WINDOW (obj->window), "ECE486/586 PDP8 Project");

// call funtion that makes labels

    create_labels(obj);
    create_buttons(obj);
    create_buffers(obj);
    create_radio_buttons( obj);
    set_radio_buttons(obj);
    create_text_boxes(obj);
    create_entrybox (obj);
    radio_button_callbacks(obj);
    create_buttons_callbacks(obj);
    entry_box_cb(obj);
    set_grid(obj);

//Init the system
obj->coherance_vars = malloc( sizeof(struct shared_vars) );
init_system(obj->copy_argc, obj->copy_argv, obj->coherance_vars);	//Initialize the simulator
//Start the memory page window at page 0
print_memory_page(0);
print_memory_list();
update_memory_buffer(obj);

    gtk_container_add (GTK_CONTAINER (obj->window), GTK_WIDGET (obj->grid));
    gtk_widget_show_all (obj->window);
}

void update_labels(g_items* object) {
uint8_t buffer_size = 4;
char PC_text[buffer_size];
char AC_text[buffer_size];
char CPMA_text[buffer_size];
char IR_text[buffer_size];
char Link_text[buffer_size];
char MB_text[buffer_size];

sprintf(PC_text, "%04o", object->coherance_vars->registers_ptr->PC);
sprintf(AC_text, "%04o", object->coherance_vars->registers_ptr->AC);
sprintf(CPMA_text, "%04o", object->coherance_vars->registers_ptr->CPMA);
sprintf(IR_text, "%01o", object->coherance_vars->registers_ptr->IR);
sprintf(Link_text, "%01o", object->coherance_vars->registers_ptr->link_bit);
sprintf(MB_text, "%04o", object->coherance_vars->registers_ptr->MB);

   gtk_label_set_text(GTK_LABEL (object->PC_value), PC_text);
   gtk_label_set_text(GTK_LABEL (object->Accumulator_value), AC_text);
   gtk_label_set_text(GTK_LABEL (object->CPMA_value), CPMA_text);
   gtk_label_set_text(GTK_LABEL (object->IR_value), IR_text);
   gtk_label_set_text(GTK_LABEL (object->Link_value), Link_text);
   gtk_label_set_text(GTK_LABEL (object->Memory_Buffer_value), MB_text);
}

gui.h
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** gui.h
******************************************************************************/

#ifndef _GUI_H
#define _GUI_H

#include <gtk/gtk.h>
#include <stdio.h>
#include <stdlib.h>
#include "cpu.h"

typedef struct g_tag
{
    GtkWidget *window;
    GtkWidget *grid;
 // top buttons
    GtkWidget * run_button, *step, *show_breakpoints, * exit_button;
// name of all labels
    GtkWidget *pagenum, *label, *PC_label, *Accumulator_label, *CPMA_label;
    GtkWidget *Mesages_label, *IR_label, *Link_label, *Memory_Buffer_label;
    GtkWidget *memory_entry_label, *SR_label;

// name if labels to be changed with the values of the registers
    GtkWidget *value, *PC_value, *Accumulator_value, *CPMA_value;
    GtkWidget *IR_value, *Link_value, *Memory_Buffer_value;

// windows, buffers
    GtkWidget *scrolled_window, * scrolled_msg, *text_view, *messages_txt;
    GtkWidget *trace_text_window, *trace_text_view;

// buffers
    GtkTextBuffer *buffer, *msgbuff, *trace_text_buffer;

// Breakpoint and Trace windows
    GtkWidget *BreakP_entry,*Trace_entry;
    GtkWidget *memory_entry, *SR_entry, *page_number_entry;;

// Buttons
    GtkWidget *radio_set_BP, *radio_clear_BP,*radioB_SetTr;
    GtkWidget *radioB_ClrTr, * display_memory_page, * display_lst_file; // radio buttons
    GtkWidget * memory_pages, *memory_trace, *branch_trace;

// file descriptor for screen
    GFile *FP;
    gchar *fname;

// Local stuff
    int copy_argc;
    char ** copy_argv;
    struct shared_vars* coherance_vars;
} g_items;

// PROTOTYPES
void create_labels(g_items * obj);
void create_buttons(g_items* obj);
void create_entrybox (g_items* obj);
void set_grid(g_items * obj);
void create_buffers(g_items * obj);
void create_text_boxes (g_items * obj);
void create_radio_buttons(g_items* obj);
void set_radio_buttons( g_items *obj);
void radio_button_callbacks( g_items * obj);
void create_buttons_callbacks(g_items* obj);
void activate (GtkApplication *app, gpointer data);
void update_labels(g_items*);

#endif

kb_input.c
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** 12 FEB 2015
** kb_input.c - Implements non-blocking keyboard I/O
**
** The functions in this file were created from these references:
** http://www.cs.cmu.edu/afs/cs/academic/class/15492-f07/www/pthreads.html#CREATIONTERMINATION
** http://cc.byexamples.com/2007/04/08/non-blocking-user-input-in-loop-without-ncurses/
** http://stackoverflow.com/questions/717572/how-do-you-do-non-blocking-console-i-o-on-linux-in-c
******************************************************************************/

#include "kb_input.h"

/******************************************************************************
** THIS FUNCTION RUNS IN A THREAD. IT READS KEYBOARD INPUT AND STORES
** THE CHARS INPUTTED.
******************************************************************************/
void* read_keyboard(void* kb_layout) {
   struct keyboard* local_kb = (struct keyboard*)kb_layout;
   int kb_return = 0;
   char inputted_char;

//Enable reading chars without hitting enter
nonblocking(NB_ENABLE);

//Begin the main reading loop
   while(!kb_return) {
      kb_return = kbhit();	//Check if key pressed

//Check to see if key was pressed
      if (kb_return != 0) {
  inputted_char = fgetc(stdin);

  pthread_mutex_lock(&keyboard_mux);
        local_kb->input_char = inputted_char;
   local_kb->input_flag = 1;
   pthread_mutex_unlock(&keyboard_mux);

        kb_return = 0;
      }

pthread_mutex_lock(&keyboard_mux);
if(local_kb->quit) kb_return = 1;
pthread_mutex_unlock(&keyboard_mux);
}
   nonblocking(NB_DISABLE);

   pthread_exit(0);
}

/******************************************************************************
** THIS FUNCTION EMULATES THE WINDOWS FUNCTION KBHIT()
******************************************************************************/
int kbhit() {
struct timeval tv;
fd_set fds;
tv.tv_sec = 0;
tv.tv_usec = 0;
FD_ZERO(&fds);
FD_SET(STDIN_FILENO, &fds); //STDIN_FILENO is 0
select(STDIN_FILENO+1, &fds, NULL, NULL, &tv);
return FD_ISSET(STDIN_FILENO, &fds);
}

/******************************************************************************
** THIS FUNCTION SETS THE TERMINAL TO NONBLOCKING MODE SO ENTER DOES NOT
** NEED TO BE PRESSED TO CAPTURE THE CHARACTER
******************************************************************************/
void nonblocking(int state) {
struct termios ttystate;

//get the terminal state
tcgetattr(STDIN_FILENO, &ttystate);

if (state==NB_ENABLE)
{
//turn off canonical mode
ttystate.c_lflag &= ~ICANON;
//minimum of number input read.
ttystate.c_cc[VMIN] = 1;
}
else if (state==NB_DISABLE)
{
//turn on canonical mode
ttystate.c_lflag |= ICANON;
}
//set the terminal attributes.
tcsetattr(STDIN_FILENO, TCSANOW, &ttystate);
}

kb_input.h
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** 12 FEB 2015
** kb_input.h
******************************************************************************/

#ifndef KB_INPUT_H
#define KB_INPUT_H

#include <stdio.h>
#include <unistd.h>
#include <termios.h>
#include <sys/select.h>
#include <pthread.h>
#include <stdlib.h>
#include <stdint.h>

#define NB_ENABLE 1
#define NB_DISABLE 0

pthread_mutex_t keyboard_mux;

struct keyboard {
   char input_char;
   uint8_t input_flag;	//0 = no input, 1 = input
   uint8_t quit;
};

void* read_keyboard(void*);
int kbhit(void);
void nonblocking(int);

#endif

main.c
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** main.c - Implements all of the glue logic. Init functions, run functions,
close functions, etc.
******************************************************************************/

#include "main.h"

#define OP_CODE_MASK 07000	// bits 0,1,2

static uint32_t clock_cycles = 0;
static uint32_t opcode_freq[OPCODE_NUM];
static uint8_t opcode_cycles[OPCODE_NUM] = {2,2,2,2,2,1,0,1};
static const char *opcode_text[OPCODE_NUM];

extern uint8_t tracepoint_reached;
regs* registers;

int main(int argc, char* argv[]) {
unsigned int i;
#ifdef GUI
    GtkApplication *app;
    g_items *obj = malloc(sizeof(*obj));
    obj->copy_argv= argv;
    obj->copy_argc = argc;
    app = gtk_application_new ("ECE.Project", G_APPLICATION_FLAGS_NONE);
    g_signal_connect (app, "activate", G_CALLBACK (activate), obj);
    g_application_run (G_APPLICATION (app), 0, NULL);
    g_object_unref (app);
#else
run_no_GUI(argc, argv);
#endif

#ifdef GUI
free(obj->coherance_vars);
   free(obj);

   remove_text_files("MEMORY_PAGE.txt");
   remove_text_files("memory_trace.txt");
   remove_text_files("branch_trace.txt");
   remove_text_files("breakpoints.txt");
#endif

// Free allocated list file memory
for(i=0; i < PAGES * WORDS_PER_PAGE; i++){
if (assembly_list[i] != NULL){
free(assembly_list[i]);
}
}

return(0);
}/*end main*/

/******************************************************************************
** REMOVES ALL OF THE TEXT FILES WE USE FOR PRINTING TO THE GUI BUFFERS
******************************************************************************/
void remove_text_files(char * buffer)
{
if(remove(buffer) == 0) {
#ifdef TRACE_DEBUG
printf("File %s deleted.\n", buffer);
#endif
}
else {
#ifdef TRACE_DEBUG
fprintf(stderr, "Error deleting the file %s.\n", buffer);
#endif
}
}

/******************************************************************************
** RUNS THE PROGRAM WITHOUT THE GUI
******************************************************************************/
void run_no_GUI(int argc, char** argv) {
int thread1_return, thread2_return;
pthread_t keyboard_thread, simulator_thread;
struct shared_vars* shared_items = malloc( sizeof(struct shared_vars) );
init_system(argc, argv, shared_items);
shared_items->ran_once = 1;

thread1_return = pthread_create(&keyboard_thread, NULL, read_keyboard, (void*)(shared_items->kb_ptr));
if(thread1_return) {
fprintf(stderr, "Keyboard thread failed\n");
exit(-1);
   }

thread2_return = pthread_create( &simulator_thread, NULL, run_program, (void*)shared_items);
if(thread2_return) {
fprintf(stderr, "Simulator thread failed\n");
exit(-2);
   }

//Run the threads
pthread_join(keyboard_thread, NULL);
pthread_join(simulator_thread, NULL);

shutdown_system(shared_items);
free(shared_items);
}

/******************************************************************************
**	RUN THE PROGRAM UNTIL BREAKPOINT/TRACEPOINT FOUND OR EXECUTION FINISHES
******************************************************************************/
void* run_program(void* args)
{
struct shared_vars* shared = (struct shared_vars*)args;

while( (shared->execution_done != 1) && (shared->breakpoint_reached != 1) && (tracepoint_reached != 1) ) {
execute_opcode(shared);
}

pthread_mutex_lock(&keyboard_mux);
shared->kb_ptr->quit = 1;
pthread_mutex_unlock(&keyboard_mux);

pthread_exit(0);
}

/******************************************************************************
**	EXECUTES A SINGLE OPCODE AND RETURNS
******************************************************************************/
void execute_opcode(struct shared_vars* shared){
const uint8_t microinstruction = 7;
char instruct_text[80];
uint8_t subgroup_returns[3];
uint8_t subgroup_taken;	//Will be 0 if branch not taken, 1 if taken
uint16_t current_PC;	//Used for the branch trace file
uint16_t current_instruction;
uint8_t addressing_mode;

current_instruction = mem_read(registers->PC, INSTRUCTION_FETCH);	// load the next instruction

#ifdef GUI
//Don't stop on a breakpoint when stepping
//Breakpoint serviced allows a user to run again a after a breakpoint was reached
if( (current_instruction & MEMORY_BREAKPOINT_BIT) && !(shared->step_or_run) &&
!(shared->breakpoint_serviced) ) {
shared->breakpoint_reached = 1;
goto EXIT;
}
else {
shared->breakpoint_serviced = 0;
}
#endif

registers->PC++;	// increment the PC
registers->IR = (current_instruction >> 9) & 0x7;	// Only grab the 3 opcode bits

//Microinstructions don't have indirect or auto increment modes
//Set the addressing mode to direct to not add additional cycles onto micro ops
if(registers->IR != microinstruction) {
addressing_mode = EffAddCalc(current_instruction, registers);	// Load the CPMA with effective address
}
else {
addressing_mode = DIRECT_MODE;
}

/* !update trace file here for instruction read! */
switch(current_instruction & OP_CODE_MASK){
case OP_CODE_AND:
AND(registers);
strcpy(instruct_text, "AND");
opcode_freq[0]++;
break;
case OP_CODE_TAD:
TAD(registers);
strcpy(instruct_text, "TAD");
opcode_freq[1]++;
break;
case OP_CODE_ISZ:
ISZ(registers);
strcpy(instruct_text, "ISZ");
opcode_freq[2]++;
break;
case OP_CODE_DCA:
DCA(registers);
strcpy(instruct_text, "DCA");
opcode_freq[3]++;
break;
case OP_CODE_JMS:
JMS(registers);
strcpy(instruct_text, "JMS");
opcode_freq[4]++;
break;
case OP_CODE_JMP:
JMP(registers);
strcpy(instruct_text, "JMP");
opcode_freq[5]++;
break;
case OP_CODE_IO:
opcode_freq[6]++;

switch(current_instruction & IO_OPCODE_BITS_MASK) {
case IO_OPCODE_KCF_BITS:
KCF(shared->kb_ptr);
strcpy(instruct_text, "KCF");
break;
case IO_OPCODE_KSF_BITS:
KSF(registers, shared->kb_ptr);
strcpy(instruct_text, "KSF");
break;
case IO_OPCODE_KCC_BITS:
KCC(registers, shared->kb_ptr);
strcpy(instruct_text, "KCC");
break;
case IO_OPCODE_KRS_BITS:
KRS(registers, shared->kb_ptr);
strcpy(instruct_text, "KRS");
break;
case IO_OPCODE_KRB_BITS:
KRB(registers, shared->kb_ptr);
strcpy(instruct_text, "KRB");
break;
case IO_OPCODE_TFL_BITS:
TFL(registers);
strcpy(instruct_text, "TFL");
break;
case IO_OPCODE_TSF_BITS:
TSF(registers);
strcpy(instruct_text, "TSF");
break;
case IO_OPCODE_TCF_BITS:
TCF(registers);
strcpy(instruct_text, "TCF");
break;
case IO_OPCODE_TPC_BITS:
TPC(registers);
strcpy(instruct_text, "TPC");
break;
case IO_OPCODE_TLS_BITS:
TLS(registers);
strcpy(instruct_text, "TLS");
break;
}
break;
case OP_CODE_MICRO:
opcode_freq[7]++;
instruct_text[0] = '\0'; // intialize string as empty
switch(current_instruction & MICRO_INSTRUCTION_GROUP_BIT){
case 0:	// Group 1
// Go through the bits and exeucute in sequence if high
if((current_instruction & MICRO_INSTRUCTION_BITS_MASK) == 0){
break;	// NOP instruction
}
if((current_instruction & MICRO_INSTRUCTION_CLA_BITS) == MICRO_INSTRUCTION_CLA_BITS){
CLA(registers);
strcat(instruct_text, "CLA ");
}
if((current_instruction & MICRO_INSTRUCTION_CLL_BITS) == MICRO_INSTRUCTION_CLL_BITS){
CLL(registers);
strcat(instruct_text, "CLL ");
}
if((current_instruction & MICRO_INSTRUCTION_CMA_BITS) == MICRO_INSTRUCTION_CMA_BITS){
CMA(registers);
strcat(instruct_text, "CMA ");
}
if((current_instruction & MICRO_INSTRUCTION_CML_BITS) == MICRO_INSTRUCTION_CML_BITS){
CML(registers);
strcat(instruct_text, "CML ");
}
if((current_instruction & MICRO_INSTRUCTION_IAC_BITS) == MICRO_INSTRUCTION_IAC_BITS){
IAC(registers);
strcat(instruct_text, "IAC ");
}
if((current_instruction & MICRO_INSTRUCTION_RAR_BITS) == MICRO_INSTRUCTION_RAR_BITS){
if((current_instruction & MICRO_INSTRUCTION_RTR_BITS) == MICRO_INSTRUCTION_RTR_BITS){
RTR(registers);
strcat(instruct_text, "RTR ");
} else {
RAR(registers);
strcat(instruct_text, "RAR ");
}
}
if((current_instruction & MICRO_INSTRUCTION_RAL_BITS) == MICRO_INSTRUCTION_RAL_BITS){
if((current_instruction & MICRO_INSTRUCTION_RTL_BITS) == MICRO_INSTRUCTION_RTL_BITS){
RTL(registers);
strcat(instruct_text, "RTL ");
} else {
RAL(registers);
strcat(instruct_text, "RAL ");
}
}
break;

case MICRO_INSTRUCTION_GROUP_BIT:	// Group 2
//OR subgroup if bit 3 is not set and bits 0-2 are not set
if( !(current_instruction & MICRO_GROUP2_SUBGROUP_BIT) && !(current_instruction & 07) ) {
// Set returns to 0 initially
subgroup_returns[0] = subgroup_returns[1] = subgroup_returns[2] = 0;
if((current_instruction & MICRO_INSTRUCTION_SMA_BITS) == MICRO_INSTRUCTION_SMA_BITS){
subgroup_returns[0] = SMA(registers);
strcat(instruct_text, "SMA ");
}
if((current_instruction & MICRO_INSTRUCTION_SZA_BITS) == MICRO_INSTRUCTION_SZA_BITS){
subgroup_returns[1] = SZA(registers);
strcat(instruct_text, "SZA ");
}
if((current_instruction & MICRO_INSTRUCTION_SNL_BITS) == MICRO_INSTRUCTION_SNL_BITS){
subgroup_returns[2] = SNL(registers);
strcat(instruct_text, "SNL ");
}
subgroup_taken = 0;
current_PC = registers->PC;
//If any in a sequence would skip, then skip
if(subgroup_returns[0] || subgroup_returns[1] || subgroup_returns[2]) {
registers->PC++;
subgroup_taken = 1;
}
write_branch_trace(current_PC, current_PC + 1, conditional_text, subgroup_taken);
}
//AND subgroup if bit 3 is set and bits 0-2 are not set
else if( current_instruction & MICRO_GROUP2_SUBGROUP_BIT ) {
//Set to 1 initially so it passes the AND at the end
subgroup_returns[0] = 1;
subgroup_returns[1] = 1;
subgroup_returns[2] = 1;

if((current_instruction & MICRO_INSTRUCTION_SPA_BITS) == MICRO_INSTRUCTION_SPA_BITS){
subgroup_returns[0] = SPA(registers);
strcat(instruct_text, "SPA ");
}
if((current_instruction & MICRO_INSTRUCTION_SNA_BITS) == MICRO_INSTRUCTION_SNA_BITS){
subgroup_returns[1] = SNA(registers);
strcat(instruct_text, "SNA ");
}
if((current_instruction & MICRO_INSTRUCTION_SZL_BITS) == MICRO_INSTRUCTION_SZL_BITS){
subgroup_returns[2] = SZL(registers);
strcat(instruct_text, "SZL ");
}

subgroup_taken = 0;
current_PC = registers->PC;
//If all in sequence are skip, then skip
if(subgroup_returns[0] && subgroup_returns[1] && subgroup_returns[2]) {
registers->PC++;
subgroup_taken = 1;
}
write_branch_trace(current_PC, current_PC + 1, conditional_text, subgroup_taken);
}

//SKP will run along with SPA, SNA or SZL if bits 3-5 are not checked
if((current_instruction & 07770) == MICRO_INSTRUCTION_SKP_BITS){
SKP(registers);
strcat(instruct_text, "SKP ");
}
if((current_instruction & MICRO_INSTRUCTION_CLA_BITS) == MICRO_INSTRUCTION_CLA_BITS){
CLA(registers);
strcat(instruct_text, "CLA ");
}
if((current_instruction & MICRO_INSTRUCTION_OSR_BITS) == MICRO_INSTRUCTION_OSR_BITS){
OSR(registers);
strcat(instruct_text, "OSR ");
}
if((current_instruction & MICRO_INSTRUCTION_HLT_BITS) == MICRO_INSTRUCTION_HLT_BITS){
HLT(shared->kb_ptr);
shared->execution_done = 1;
strcat(instruct_text, "HLT ");
}
break;
}
break;
}
//printf("Instruction = %s\n", instruct_text);

#ifdef MEMORY_DEBUG
switch (addressing_mode){
case 0:
printf("Opcode: %u Addressing mode: %u %s\n", registers->IR,0, "Direct Mode, \tZero Page");
break;
case 1:
printf("Opcode: %u Addressing mode: %u %s\n", registers->IR,1, "Direct Mode, \tCurrent Page");
break;
case 2:
printf("Opcode: %u Addressing mode: %u %s\n", registers->IR,2, "Indirect Mode, \tZero Page");
break;
case 3:
printf("Opcode: %u Addressing mode: %u %s\n", registers->IR,3, "Indirect Mode, \tCurrent Page");
break;
case 4:
printf("Opcode: %u Addressing mode: %u %s\n", registers->IR,4, "Indirect Mode, \tAuto Indexing");
break;
default:
break;
}
#endif

#ifdef DEBUG
printf("Cycles Before = %u, ", clock_cycles);
#endif

if(addressing_mode == DIRECT_MODE ||addressing_mode == (DIRECT_MODE +1) ) {
clock_cycles += opcode_cycles[registers->IR];
}
else if(addressing_mode == INDIRECT_MODE || addressing_mode == (INDIRECT_MODE+1)) {
clock_cycles += opcode_cycles[registers->IR] + 1;
}
else {	/* Autoincrement mode */
clock_cycles += opcode_cycles[registers->IR] + 2;
}

#ifdef DEBUG
printf("Cycles After = %u\n", clock_cycles);
printf("After opcode: %s - %04o, AC: %04o, Link: %01o, MB: %04o, PC: %04o, CPMA: %04o\n\n", instruct_text, current_instruction & MEMORY_MASK,
registers->AC & CUTOFF_MASK, registers->link_bit, registers->MB & CUTOFF_MASK, registers->PC, registers->CPMA);
#endif

#ifdef GUI
EXIT:
#endif
return;	//For exiting on breakpoint
} // end run_program

/******************************************************************************
**	MALLOCS STRUCTS, INITS MEMORY, AND OPENS TRACE FILES
******************************************************************************/
void init_system(int argc, char* argv[], struct shared_vars* shared) {
int trace_return;
int i;
int branch_trace_open;

//Malloc structs needed in g_items
registers = malloc(sizeof(regs));
shared->registers_ptr = registers;
shared->kb_ptr = malloc(sizeof(struct keyboard));
shared->kb_ptr->input_flag = 0;
shared->kb_ptr->quit = 0;
shared->execution_done = 0;
shared->breakpoint_reached = 0;
shared->step_or_run = RUN;
shared->ran_once = 0;
shared->branch_trace = 1;
shared->last_mem_page = 0;

//For RAND in TSF
srand(time(NULL));

mem_init();
fill_memory(argc, argv);

//can capture return values to verify fopen && fclose
trace_return = trace_init();
if(trace_return) {
printf("Unable to open trace file. Exiting\n");
exit(-1);
}
branch_trace_open = branch_trace_init();
if(branch_trace_open) exit(branch_trace_open);

#ifdef MEMORY_DEBUG
mem_print_valid();
#endif
reset_regs(registers);	// initialize the CPU

for(i = 0; i < OPCODE_NUM; i++) {
opcode_freq[i] = 0;
}

opcode_text[0] = "AND";
opcode_text[1] = "TAD";
opcode_text[2] = "ISZ";
opcode_text[3] = "DCA";
opcode_text[4] = "JMS";
opcode_text[5] = "JMP";
opcode_text[6] = "I\\O";
opcode_text[7] = "Micro Ops";
}

/******************************************************************************
** FILLS MEMORY WITH INPUTTED MEMORY FILE
@CHANGELOG:
JSP:
-Modified argv count and first 'if' statement to take tracefile arg
-Added tracefile generation functions
******************************************************************************/
void fill_memory(int argc, char* argv[]) {
const uint8_t data_mask = 0x3F;	/* Keep lower 6 bits of the upper/lower bytes */
const uint8_t address_mask = 0x40;	/* Mask to check the address bit */
const uint8_t high_shift	= 6;	/* Shifts the high byte */
FILE* program_file;
FILE* list_file;
uint16_t high_byte, low_byte, word_value;
static uint16_t address = 0;
char list_filename[256], assembly_string[256];
unsigned int i, j, addr, value, line_number;

int return1, return2, c;
return1 = return2 = 0;

if(argc == 3) {
program_file = fopen(argv[1], "r");
trace_name = argv[2];
}
else {
printf("Please provide a valid program filename to use with the simulator.\n");
printf("FORMAT:\n PDP_sim <input_file> <trace_file>\n");
exit(-1);
}
if(program_file == NULL) {
printf("The entered program filename does not exist.\n");
exit(-2);
}

/* Main loop that loads the memory */
for(;;) {
/* Grab up to a maximum of three octal values */
return1 = fscanf(program_file, "%3" SCNo16, &high_byte);
return2 = fscanf(program_file, "%3" SCNo16, &low_byte);

if(return1 == EOF || return2 == EOF)
break;

word_value = ((high_byte & data_mask) << high_shift) | (low_byte & data_mask);

#ifdef FILL_DEBUG
printf("From file - high: %o, low: %o\n", high_byte, low_byte);
printf("Word_value: %o\n", word_value);
#endif

if(high_byte & address_mask) {
address = word_value;
#ifdef FILL_DEBUG
printf("Address changed to: %o\n", address);
#endif
}
else {
memory[address] = word_value | MEMORY_VALID_BIT;
#ifdef FILL_DEBUG
printf("Memory value at address %o set to: %o\n", address, memory[address]);
#endif
address++;
}

#ifdef FILL_DEBUG
printf("\n");
#endif
}/*end for*/

// Initialize array of list file strings to NULL
for(i=0; i < PAGES * WORDS_PER_PAGE; i++){
assembly_list[i] = NULL;
}

// Determine list filename by replacing .obj with .lst
strcpy(list_filename, argv[1]);
strcpy(list_filename + strlen(argv[1]) - 3, "lst");
//	printf("list file name is: %s\n", list_filename);

// Load in list file
list_file = fopen(list_filename, "r");
if(list_file != NULL){
while(fscanf(list_file, "%i", &line_number) != EOF){
do { // read the next character that isn't a space
c = fgetc(list_file);
} while(c == ' ' || c == '\t');
ungetc(c, list_file); // put the non-space character back
if (c >= '0' && c <= '9'){ // if this starts with a number, then it's valid data or code
//	printf("%i ", line_number);
fscanf(list_file, "%o %o", &addr, &value);
//	printf("%o %o ", addr, value);
do { // read the next character that isn't a space
c = fgetc(list_file);
} while(c == ' ' || c == '\t');
ungetc(c, list_file); // put the non-space character back
fgets(assembly_string, 255, list_file);
assembly_string[strlen(assembly_string) - 1] = '\0'; // remove terminating '\n'
assembly_list[addr] = (char*) malloc(strlen(assembly_string) + 1 * sizeof(char));
strcpy(assembly_list[addr], assembly_string);
for(j=0; j < strlen(assembly_list[addr]); j++){ // convert tabs to spaces
if(assembly_list[addr][j] == '\t'){
assembly_list[addr][j] = ' ';
}
}
//	printf("%s\n", assembly_list[addr]);
} else { // otherwise read the rest of the line, ignore it, and continue
fgets(assembly_string, 255, list_file);
}
}
fclose(list_file);
}
fclose(program_file);
}

/******************************************************************************
**	PRINTS THE REQUESTED STATS
******************************************************************************/
void print_stats(void) {
int i;
uint32_t executed_total = 0;

printf("*************************************************************\n");
printf("***********************PRINTING STATS************************\n");
printf("*************************************************************\n");
printf("Total clock cycles = %u\n", clock_cycles);

for(i = 0; i < OPCODE_NUM; i++) {
printf("%s was executed %u times\n", opcode_text[i], opcode_freq[i]);
executed_total += opcode_freq[i];
}

printf("The total number of opcodes executed = %u\n", executed_total);
}

/******************************************************************************
**	FREES MEMORY, CLOSES TRACE FILES AND PRINTS INFORMATION
******************************************************************************/
void shutdown_system(struct shared_vars* shared) {
free(shared->registers_ptr);
free(shared->kb_ptr);
if(shared->ran_once) {
#ifdef DEBUG
mem_print_valid();
#endif
print_stats();
}
trace_close();
close_branch_trace();
}
/******************************************************************************
**	EOF
******************************************************************************/

main.h
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** main.h
******************************************************************************/

#ifndef MAIN_H
#define MAIN_H

//#define FILL_DEBUG
//#define DEBUG
#define DEBUG_GUI
//#define GUI

#ifdef GUI
#include <gtk/gtk.h>
#include "gui.h"
#include "callback.h"
#endif

#include <stdio.h>
#include <stdlib.h>
#include <stdint.h>
#include <string.h>
#include "memory.h"

#include "kb_input.h"
#include "branch_trace.h"

#define OPCODE_NUM 8
#define STEP 1
#define RUN 0

//This struct holds variables that both the GUI and non GUI versio need
typedef struct shared_vars {
regs *registers_ptr;
   struct keyboard* kb_ptr;
uint8_t breakpoint_reached;
uint8_t breakpoint_serviced;	//Used to run again after a breakpoint was reached
uint8_t step_or_run;
uint8_t execution_done;
uint8_t ran_once;
uint8_t branch_trace;	//Will be a 1 if branch trace last screen loaded
int last_mem_page;
} shared_vars;

int main(int argc, char* argv[]);
void run_no_GUI(int, char**);
void* run_program(void*);
void execute_opcode(struct shared_vars*);
void init_system(int argc, char* argv[], struct shared_vars*);
void fill_memory(int argc, char* argv[]);	/* Fills memory at bootup */
void print_stats(void);
void shutdown_system(struct shared_vars*);
void remove_text_files(char * buffer);

#endif

memory.c
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken Benderly, J.S. Peirce
**
** 21 JANUARY 2015
** MEMORY.C	IMPLEMENTATION FILE FOR MEMORY OP FUNCTIONS
******************************************************************************/
#include "memory.h"
#include "cpu.h"

uint8_t tracepoint_reached;
uint8_t tracepoint_number;
extern regs* registers;

/******************************************************************************
**	READ FROM MEMORY
**	FOR READ_OR_FETCH VARIABLE: 0 = DATA READ	1 = INSTRUCTION_FETCH
******************************************************************************/
uint16_t mem_read(uint16_t to_convert, uint8_t read_or_fetch){
uint16_t page;
uint8_t offset;
uint16_t converted;
uint16_t retval;

//parse address from CPMA
page = (0b0000111110000000 & to_convert);//0xF80
offset = (0b0000000001111111 & to_convert);//0x7F
converted = (page + offset);
#ifdef MEMORY_DEBUG
printf("UNCONVERTED:\n");
printf("Address:\n\tHEX: 0x%x\tOCTAL: %o\tDEC: %u\n",to_convert,to_convert,to_convert);
printf("CONVERTED:\n");
printf("Address:\n\tHEX: 0x%x\tOCTAL: %o\tDEC: %u\n",converted,converted,converted);
printf("Page:\n\tHEX: 0x%x\tOCTAL: %o\tDEC: %u\n",page,page,page);
printf("Offset:\n\tHEX: 0x%x\tOCTAL: %o\tDEC: %u\n",offset,offset,offset);
#endif

//Print to trace file and handle the fetch accordingly
if(read_or_fetch == DATA_READ) {
//First check if a tracepoint has been reached
retval = memory[converted];
if(retval & MEMORY_TRACEPOINT_BIT) {
tracepoint_reached = 1;
tracepoint_number = converted;
}

//Remove internal state bits for read
retval &= CUTOFF_MASK;
#ifdef PRETTY_PRINT
fprintf( trace_file, "DR %04o\n", converted);
#else
fprintf( trace_file, "0 %04o\n", converted);
#endif
}
else if(read_or_fetch == INSTRUCTION_FETCH) {
retval = memory[converted];
#ifdef PRETTY_PRINT
fprintf( trace_file, "IF %04o\n", converted);
#else
fprintf( trace_file, "2 %04o\n", converted);
#endif
}
else {
fprintf( trace_file, "Read type not recognized\n");
}

return retval;
}/*end mem_read()*/

/******************************************************************************
**	WRITE TO MEMORY
******************************************************************************/
void mem_write(uint16_t to_convert, uint16_t data){
uint16_t page;
uint8_t offset;
uint16_t converted;
//parse address from CPMA
page = (0b0000111110000000 & to_convert);//0xF80
offset = (0b0000000001111111 & to_convert);//0x7F
converted = (page + offset);
#ifdef MEMORY_DEBUG
printf("UNCONVERTED:\n");
printf("Address:\n\tHEX: 0x%x\tOCTAL: %o\tDEC: %u\n",to_convert,to_convert,to_convert);
printf("CONVERTED:\n");
printf("Address:\n\tHEX: 0x%x\tOCTAL: %o\tDEC: %u\n",converted,converted,converted);
printf("Page:\n\tHEX: 0x%x\tOCTAL: %o\tDEC: %u\n",page,page,page);
printf("Offset:\n\tHEX: 0x%x\tOCTAL: %o\tDEC: %u\n",offset,offset,offset);
#endif

/* Write to trace file */
#ifdef PRETTY_PRINT
fprintf( trace_file, "DW %04o\n", converted);
#else
fprintf( trace_file, "1 %04o\n", converted);
#endif

//Check if tracepoint is set
if(memory[converted] & MEMORY_TRACEPOINT_BIT) tracepoint_reached = 1;

memory[converted] &= ~MEMORY_MASK;	//Clear the data field
memory[converted] |= data & MEMORY_MASK;

#ifdef MEMORY_DEBUG
printf("CALLEE->WROTE: %o to: %o IN OCTAL\n", data, converted);
printf("CALLEE->WROTE: %u to: %u IN UNSIGNED DEC\n", data, converted);
#endif
}/*end mem_write*/

/******************************************************************************
**	INITIALIZE THE MEMORY
******************************************************************************/
void mem_init(void){
unsigned int i;

for(i=0; i < PAGES * WORDS_PER_PAGE; i++){
memory[i] &= ~(MEMORY_VALID_BIT | MEMORY_BREAKPOINT_BIT); // clear valid and breakpoint bits
}
} // end mem_init

/******************************************************************************
**	PRINT ALL VALID MEMORY LOCATIONS
******************************************************************************/
void mem_print_valid(void){
unsigned int i;

printf("******************************PRINTING VALID MEMORY**************************\n");
printf("Address Contents\n");
printf("------- --------\n");
for(i=0; i < PAGES * WORDS_PER_PAGE; i++){
if (memory[i] & MEMORY_VALID_BIT){
printf("%04o %04o\n", i, memory[i] & MEMORY_MASK);
}
}
printf("\n");
} // end mem_print_valid

/******************************************************************************
**	OPEN THE TRACEFILE TO APPEND, START AT BEGINNING OF FILE: "a+"
******************************************************************************/
int trace_init(){
int ret_val;
trace_file = fopen(trace_name, "w");

if(trace_file == NULL){
#ifdef TRACE_DEBUG
printf("ERROR: Unable to open memory trace file: %s\n", trace_name);
#endif
ret_val = -1;
}/*end if*/
else{
#ifdef TRACE_DEBUG
printf("Memory trace file: %s opened successfully\n", trace_name);
#endif
ret_val=0;
}/*end else*/
return ret_val;
}/*end trace_init()*/

/******************************************************************************
** WRITES TO THE MEMORY TRACE FILE IN THE MIDDLE OF THE PROGRAM
******************************************************************************/
void update_memory_trace(void) {
fclose(trace_file);
trace_file = fopen(trace_name, "a");

#ifdef TRACE_DEBUG
if(trace_file == NULL) {
printf("ERROR: Failed to open memory trace file for append.\n");
}
else {
printf("Branch trace file opened successfully for append\n");
}
#endif
}

/******************************************************************************
** CALL THIS FUNCTION AT COMPLETION OF PROGRAM TO CLOSE TRACEFILE
** TODO: MAY NOT BE A BAD IDEA TO OPEN/CLOSE EACH TIME WE WRITE OUT?
******************************************************************************/
int trace_close(){
int ret_val;
ret_val = fclose(trace_file);
return ret_val;
}/*end close_trace()*/

/******************************************************************************
**	RETURN EFFECTIVE ADDRESS AT ZERO PAGE
******************************************************************************/
uint16_t zeropage (uint16_t instruction)
{
    return instruction & OFFSET_MASK;
}

/******************************************************************************
**	RETURN EFFECTVE ADDRESS AT THE CURRENT PAGE
******************************************************************************/
uint16_t currentpage (uint16_t instruction, regs* reg)
{
    return ( (reg->PC & PAGE_MASK) | (instruction & OFFSET_MASK) );
}

/******************************************************************************
**	DECODE ADDRESS
******************************************************************************/
// Check bit 4 (on PDP8 ) to federmine current page or zero page mode

uint16_t getaddress(uint16_t instruction,regs* reg, uint8_t * page)
{
uint16_t retval;
if (PageMode(instruction))
   {
   retval = currentpage(instruction, reg);
  *page=1;
   }
   else
   {
   retval = zeropage(instruction);
*page=0;
   }

return retval;
}

/******************************************************************************
**	CALCULATE THE EFFECTIVE ADDRESS
**	RETURNS 0 FOR DIRECT ADDRESSING page 0
** 1 FOR DIRECT ADDRESSING CURRENT PAGE
** 2 FOR INDIRECT ADDRESSING PAGE O
** 3 FOR INDIRECT CURRENT PAGE,
** 4 FOR AUTOINCREMENT
******************************************************************************/
uint8_t EffAddCalc(uint16_t instruction, regs* reg)
{
uint16_t ptr_address, indirect_address;
uint8_t addressing_mode, page_mode;

page_mode =0;
    if(AddrMode(instruction))
    {
        /* Indirect mode
        gets the ponter address*/
ptr_address = getaddress(instruction, reg, & page_mode);
        indirect_address = mem_read(ptr_address, DATA_READ);

addressing_mode = INDIRECT_MODE+ page_mode;

        // check if address is the range of auto indexing
        if (ptr_address >= 010 && ptr_address <= 017)
        {
        addressing_mode = AUTOINCREMENT_MODE;
        ++indirect_address;
        mem_write(ptr_address, indirect_address );

        }

        reg->CPMA= indirect_address;
    }
    else
    {
        // not indirect just store the value
        reg->CPMA = getaddress(instruction, reg,& page_mode);
 addressing_mode = DIRECT_MODE + page_mode;
    }

return addressing_mode;
}

/******************************************************************************
**	SETS A BREAKPOINT IN MEMORY
******************************************************************************/
void set_breakpoint(uint16_t breakpoint_address) {
memory[breakpoint_address] |= MEMORY_BREAKPOINT_BIT;
}

/******************************************************************************
**	REMOVES A BREAKPOINT FROM MEMORY
******************************************************************************/
void remove_breakpoint(uint16_t breakpoint_address) {
memory[breakpoint_address] &= ~MEMORY_BREAKPOINT_BIT;
}

/******************************************************************************
**	SETS A TRACEPOINT IN MEMORY
******************************************************************************/
void set_tracepoint(uint16_t tracepoint_address) {
memory[tracepoint_address] |= MEMORY_TRACEPOINT_BIT;
}

/******************************************************************************
**	REMOVES A TRACEPOINT FROM MEMORY
******************************************************************************/
void remove_tracepoint(uint16_t tracepoint_address) {
memory[tracepoint_address] &= ~MEMORY_TRACEPOINT_BIT;
}

/******************************************************************************
**	PRINTS A PAGE OF MEMORY TO A TEXT FILE NAMED MEMORY_PAGE.TXT
** CAN BE OPENED BY THE GUI TO PRINT TO THE TEXT WINDOW
******************************************************************************/
void print_memory_page(int page_number) {
uint16_t page_base_address, page_max_address, index;
uint16_t data_values[8];
FILE* memory_print_file;
char* memory_print_file_name = "MEMORY_PAGE.txt";

memory_print_file = fopen(memory_print_file_name, "w");

if(memory_print_file == NULL) {
printf("Error opening MEMORY_PAGE.txt\n");
}
else {
//Move the 5 bit page number to the page bits a PDP8 address
page_base_address = (page_number & 0x1F) << 7;
page_max_address = ((page_number + 1) & 0x3F) << 7;

fprintf(memory_print_file, " \t| PAGE: %o \t\t |\n", page_number);
fprintf(memory_print_file, " \t| LSB OCTAL DIGIT OF ADDRESS |\n");
fprintf(memory_print_file, " \t|-----------------------------------------------------------------------|\n");
fprintf(memory_print_file, " \t| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 |\n");
fprintf(memory_print_file, "MSB |-----------------------------------------------------------------------|\n");
for(index = page_base_address; index < page_max_address; index += 8) {
//Grab the data values from memory
data_values[0] = memory[index] & MEMORY_MASK;
data_values[1] = memory[index + 1] & MEMORY_MASK;
data_values[2] = memory[index + 2] & MEMORY_MASK;
data_values[3] = memory[index + 3] & MEMORY_MASK;
data_values[4] = memory[index + 4] & MEMORY_MASK;
data_values[5] = memory[index + 5] & MEMORY_MASK;
data_values[6] = memory[index + 6] & MEMORY_MASK;
data_values[7] = memory[index + 7] & MEMORY_MASK;

fprintf(memory_print_file, "%03o | %04o %04o %04o %04o %04o %04o %04o %04o|\n",
(index & 07770) >> 3, data_values[0], data_values[1], data_values[2],
data_values[3], data_values[4], data_values[5], data_values[6],
data_values[7]);
}
fprintf(memory_print_file, " |------------------------------------------------------------------------|\n");
}

fclose(memory_print_file);
}

/******************************************************************************
**	PRINTS VALID MEMORY ALONG WITH THE LIST FILE ASSEMBLBY CODE AND COMMENTS
** CAN BE OPENED BY THE GUI TO PRINT TO THE TEXT WINDOW
******************************************************************************/
void print_memory_list(void) {
FILE* memory_print_file;
char* memory_print_file_name = "MEMORY_LIST.txt";
unsigned int i;

memory_print_file = fopen(memory_print_file_name, "w");

if(memory_print_file == NULL) {
printf("Error opening MEMORY_LIST.txt\n");
}
else {
for(i=0; i < PAGES * WORDS_PER_PAGE; i++){
if(memory[i] & MEMORY_VALID_BIT){
// first print breakpoint, tracepoint bits
if(memory[i] & MEMORY_BREAKPOINT_BIT){
fprintf(memory_print_file, "b");
} else {
fprintf(memory_print_file, " ");
}
if(memory[i] & MEMORY_TRACEPOINT_BIT){
fprintf(memory_print_file, "t ");
} else {
fprintf(memory_print_file, " ");
}
// print current PC indicator, or a bunch of spaces
if(i == registers->PC){
fprintf(memory_print_file, "==> ");
} else {
fprintf(memory_print_file, " ");
}

fprintf(memory_print_file, "%04o %04o", i, memory[i] & MEMORY_MASK);
if (assembly_list[i] != NULL){
fprintf(memory_print_file, " %s", assembly_list[i]);
}
fprintf(memory_print_file, "\n");
}
}
}
fclose(memory_print_file);
}

/******************************************************************************
 *	PRINT BREAKPOINTS
 *****************************************************************************/
void print_breakpoints(void){
const char* breakpoint_filename = "breakpoints.txt";
FILE * breakpoint_file;
int index = 0;
breakpoint_file = fopen(breakpoint_filename, "w");

#ifdef TRACE_DEBUG
if(breakpoint_file == NULL){
printf("File open error, does it exist?\n");
}else{
printf("File opened successfully!\n");
}//end else
#endif

fprintf(breakpoint_file, "Breakpoints set at addresses: ");
//walk memory
for(; index<(PAGES*WORDS_PER_PAGE); index++){
//if BREAKPOINT bit set, write to file
if((memory[index] & MEMORY_BREAKPOINT_BIT)){
fprintf(breakpoint_file, " %04o,", index);
#ifdef TRACE_DEBUG
printf("Wrote: %04o to: %s\n", index, breakpoint_filename);
#endif
}//end if
}//end for

fclose(breakpoint_file);
}//end print_breakpoints

/******************************************************************************
 *	EOF
 *****************************************************************************/

memory.h
/******************************************************************************
** ECE486/586 PDP-8 Simulator
** Sean Koppenhafer, Luis Santiago, Ken, J.S. Peirce
**
** 15 JANUARY 2015
** memory.h
******************************************************************************/

#include <inttypes.h>
#include <unistd.h>
#include <stdio.h>
#include "cpu.h"	//Needed for regs

#ifndef MEMORY_H
#define MEMORY_H

//#define PRETTY_PRINT

/* Total memory size is 4K */
#define WORDS_PER_PAGE 128
#define PAGES 32

#define MEMORY_MASK	0xFFF	/*Only 12 bits needed for address or a data*/
#define MEMORY_VALID_BIT	0x8000
#define MEMORY_BREAKPOINT_BIT	0x4000
#define MEMORY_TRACEPOINT_BIT 0x2000

/* For trace files */
#define DATA_READ 0
#define INSTRUCTION_FETCH 1

/* Addressing mode defines */
#define DIRECT_MODE 0
#define INDIRECT_MODE 2
#define AUTOINCREMENT_MODE 4

/* Effective address */
#define PageMode(var)	((var) & (1<<7))
#define AddrMode(var)	((var) & (1<<8))
#define OFFSET_MASK	0X7F
#define PAGE_MASK	0XF80

uint16_t memory[PAGES * WORDS_PER_PAGE];
char * assembly_list[PAGES * WORDS_PER_PAGE];
char *trace_name;
FILE *trace_file;

// Prototypes
void mem_init(void);
void mem_print_valid(void);
int trace_init();
void update_memory_trace(void);
int trace_close();
uint16_t mem_read(uint16_t to_convert, uint8_t read_or_fetch);
void mem_write(uint16_t to_convert, uint16_t data);
uint16_t zeropage(uint16_t);
uint16_t currentpage(uint16_t, regs*);
uint8_t EffAddCalc(uint16_t, regs*);

//GUI functions
void set_breakpoint(uint16_t);
void remove_breakpoint(uint16_t);
void set_tracepoint(uint16_t);
void remove_tracepoint(uint16_t);
void print_memory_page(int);
void print_memory_list(void);
void print_breakpoints(void);

/******************************************************************************
**	EOF
******************************************************************************/
#endif

makefile
CC=gcc
CFLAGS= -g -c -Wall
LDFLAGS= -pthread
SOURCES=main.c memory.c cpu.c kb_input.c branch_trace.c
OBJECTS=$(SOURCES:.c=.o)
EXECUTABLE=PDP8_sim

all: $(SOURCES) $(EXECUTABLE)

$(EXECUTABLE): $(OBJECTS)
$(CC) $(LDFLAGS) $(OBJECTS) -o $@

.c.o:
$(CC) $(CFLAGS) $< -o $@

clean:
rm -rf *~ *.o $(EXECUTABLE)

# to generate this list use: gcc -MM -g -c -Wall *.c

cpu.o: cpu.c cpu.h
main.o: main.c main.h memory.h cpu.h
memory.o: memory.c memory.h
kb_input.o: kb_input.c kb_input.h
branch_trace.o: branch_trace.c branch_trace.h

makefile.gui
CC=gcc
CFLAGS= -g -c -Wall -DGUI `pkg-config --cflags gtk+-3.0`
LDFLAGS= -pthread
GTKLINK=`pkg-config --libs gtk+-3.0`
SOURCES=main.c memory.c cpu.c kb_input.c branch_trace.c gui.c callback.c
OBJECTS=$(SOURCES:.c=.o)
EXECUTABLE=PDP8_sim

all: $(SOURCES) $(EXECUTABLE)

$(EXECUTABLE): $(OBJECTS)
$(CC) $(LDFLAGS) $(OBJECTS) -o $@ $(GTKLINK)

.c.o:
$(CC) $(CFLAGS) $< -o $@

clean:
rm -rf *~ *.o $(EXECUTABLE)

# to generate this list use: gcc -MM -g -c -Wall *.c

branch_trace.o: branch_trace.c branch_trace.h
callback.o: callback.c callback.h gui.h
cpu.o: cpu.c cpu.h kb_input.h memory.h branch_trace.h
gui.o: gui.c gui.h callback.h
kb_input.o: kb_input.c kb_input.h
kb_test.o: kb_test.c
main.o: main.c main.h memory.h cpu.h kb_input.h branch_trace.h callback.h gui.h
memory.o: memory.c memory.h cpu.h kb_input.h