ECE486/586 – PDP8 Simulator Report
Sean Koppenhafer, Ken Benderly, Luis Santiago, Steve Peirce

General Design Specifications
Our PDP8 simulator uses the octal format of output from the PAL assembler. Our simulator has a starting address of 0200 octal when executing programs. The simulator can run in the terminal, or in a GUI debugger.

Testing
We tried to tried to test all possible edge case scenarios. For the non micro instructions, there is a test case for each instruction. The only somewhat challenging test is the TAD test, since there are many edge cases. In the TAD test, carry and non-carry situations were generated to test if link register functionality worked correctly. Micro instruction tests were divided into group 1 and group 2. Group 1 micro instructions were tested for each level to be completed in order and in combinations that combined levels of instructions. Group 2 micro instructions were tested as OR group or AND group skip level one instructions with and without other instruction levels. The OR and AND group micro instructions were tested for all possible combinations of one, two, or three skip combinations either triggering or not triggering the skip.

I/O Implementation
To implement truly non-blocking I/O, we had to make our simulator multi-threaded. One thread executes the simulator, while the other thread grabs keyboard input as is it received. Because both threads begin running at the same time, keyboard input can be entered throughout the simulators execution. The input will have no effect unless the simulator thread is currently executing an instruction that checks if the keyboard is receiving input.

All I/O instructions have been implemented. The ~ character is special. The ~ character is not grabbed by the krb opcude to allow for testing of “missing” the input. The tsf opcode simulates the printer being ready by setting a counter to a randomly generated number between 1 and 10 on the first call of tsf. Subsequent calls to tsf decrement the counter by 1 until 0 is reached again. On 0, the printer is ready to print, and the opcode skips to the next instruction.

A test case has been included with the document that prints out a welcome message that asks for the users name. The user can then enter in their name (up to 8 characters) and press enter. When either 8 characters or enter has been reached, the program will print out “nice to meet you name”. All printed and stored messages take place inside of the PDP8 simulator.

GUI Debugger
The GUI debugger was implemented using gtk3. Here is a list of features that the GUI debugger has:
1. Options to step and run through the program
2. Can set and remove both breakpoints and tracepoints.
3. Button to show all breakpoints.
4. View register values once a breakpoint, tracepoint, or halt instruction has been reached when running. When stepping, register values are updated every step.
5. Ability to view any of the 32 pages of memory whenever program execution is stalled.
6. Ability to view the branch trace and memory trace results whenever the programs execution is stalled.
7. Return the memory value at a specified address.
8. Opens the list file of the object file and steps through the code in tandem with the step button.

Effective Address Calculation
The function receives a 12 bit instruction and place the effective address in the CPMA. A 12 bit instruction and a pointer tho the registers struct are passed as arguments to the effective address calculation function. The function test bit 3 of the instruction to determine if it is a direct or indirect mode instruction. Next it will test bit 4 to determine if the instruction is in the current page or the zero page. If the instruction is direct mode current page the offset in the instruction is concatenated with the current page and the value placed on the CPMA register. Similarly for direct mode zero page only the offset with leading zeros is used and the value is placed in the CPMA. If indirect mode is detected the same steps are taken to determine the value but instead of placing the value directly to the CPMA register, the value is used to do a memory read and the value from the memory read it is placed in the CPMA. Indirect address has one more feature if the address to be used for the indirect mode is stored between address 10 and 17 octal the value is auto incremented by one each access and the incremented value is used for the read and placed on the CPMA.

To test the function we used wrote a program that used all 5 addressing modes cases and tested the entire range of auto increment addresses. A second version of the previous program was slightly modified to ensure auto increment only happened with indirect mode instructions and not just in the address range.

Test Cases

Micro Instructions

group_1.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 1 micro instructions
/ Should take 27 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,
cla cll	/ clear AC and Link
nop	/ no operation
dca A	/ overwrite A, should change to zero
cma cml	/ complement AC and link, should be all 1's
dca B	/ store in B, should be 1's
cla	/ clear AC, but link is still 1
rar	/ link bit rotates to bit 0 of AC
dca C	/ store in C, should be 4000 octal
cml rtr	/ set link, link bit rotates to bit 1 of AC
dca D	/ store in D, should be 2000 octal
cml ral	/ set link, link bit rotates to bit 11 of AC
dca E	/ store in E, should be 1 octal
cml rtl	/ set link, link bit rotates to bit 10 of AC
dca F	/ store in E, should be 2 octal
iac	/ increment AC
dca G	/ should be 1
cma iac	/ complement AC, then increment AC
dca H	/ should be 0
hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 7777	/ cla will change this to zero
B, 0	/ cma will change this to 1's
C, 0	/ rar will change this to 04000
D, 0	/ rtr will change this to 02000
E, 0	/ ral will change this to 01
F, 0	/ rtl will change this to 02
G, 0	/ iac will change this to 01
H, 7777	/ iac will change this to 0

group_2_OR_test_1.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions
/ Should take 21 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test skips working first
cla cll	/ clear AC and link
tad A	/ load AC with -1
sma	/ skip on minus AC
dca B	/ overwrite B if SMA fails, should not run
cla cll	/ clear AC and link
sza	/ skip on zero AC
dca C	/ overwrite C if SZA fails, should not run
cla cll cml	/ clear AC and link, set link high
snl	/ skip on nonzero link
dca D	/ overwrite D if SZA fails, should not run

/ Test skips failing
cla cll	/ clear AC and link
sma	/ skip on minus AC
dca E	/ overwrite E if SMA fails, should run
cla cll cma	/ clear AC and link
sza	/ skip on zero AC
dca F	/ overwrite F if SZA fails, should run
cla cll	/ clear AC and link, set link high
snl	/ skip on nonzero link
dca G	/ overwrite G if SZA fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 7777	/ -1
B, 0	/ will get -1 if sma fails
C, 1	/ will get 0 if sza fails
D, 2	/ will get 0 if snl fails
E, 3	/ will get 0 when sma fails
F, 4	/ will get 7777 when sza fails
G, 5	/ will get 0 when snl fails

group_2_OR_test_2.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions
/ Should take 25 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test combos of sma and sza
cla cll cma	/ clear AC and link, load AC with -1
sma	sza	/ skip on minus AC, zero AC
dca B	/ overwrite B if SMA sza fails, should not run
cla cll	/ clear AC and link
sma sza	/ skip on minus AC, zero AC
dca C	/ overwrite C if SMA SZA fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sma sza	/ skip on minus AC, zero AC
dca D	/ overwrite C if SMA SZA fails, should run

cla cll cma	/ clear AC and link, load AC with -1
sma	snl	/ skip on minus AC, non-zero link
dca E	/ overwrite E if sma snl fails, should not run
cla cll cml	/ clear AC and link, set link high
sma snl	/ skip on minus AC, non-zero link
dca F	/ overwrite F if sma snl fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sma snl	/
dca G	/ overwrite G if sma snl fails, should run

cla cll	/ clear AC and link, load AC with -1
sza	snl	/ skip on minus AC, non-zero link
dca H	/ overwrite H if sma snl fails, should not run
cla cll cml	/ clear AC and link, set link high
sza snl	/ skip on minus AC, non-zero link
dca I	/ overwrite I if sma snl fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sza snl	/
dca J	/ overwrite J if sma snl fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
B, 0	/ should not change
C, 1	/ should not change
D, 2	/ will get 1 when sma sza fails
E, 3	/ should not change
F, 4	/ should not change
G, 5	/ will get 1 when sma snl fails
H, 6	/ should not change
I, 7	/ should not change
J, 10	/ will get 1 when sza snl fails

group_2_OR_test_3.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions
/ Should take 25 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test combos sma sza snl at the same time
cla cll cma	/ clear AC and link, load AC with -1
sma	sza snl	/ skip on minus AC, zero AC, non-zero link
dca B	/ overwrite B if SMA sza snl fails, should not run
cla cll	/ clear AC and link
sma	sza snl	/ skip on minus AC, zero AC, non-zero link
dca C	/ overwrite C if SMA SZA snl fails, should not run
cla cll iac cml	/ clear AC and link, set AC to 1, set link to 1
sma	sza snl	/ skip on minus AC, zero AC, non-zero link
dca D	/ overwrite C if SMA SZA snl fails, should not run

cla cll iac	/ clear AC and link, load AC with 1
sma	sza snl	/ skip on minus AC, zero AC, non-zero link
dca E	/ overwrite E if sma snl fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
B, 0	/ should not change
C, 1	/ should not change
D, 2	/ should not change
E, 3	/ will get 1 when sma sza snl fails

group_2_AND_test_1.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions, AND subgroup
/ Should take 19 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test skips working first
cla cll iac	/ clear AC and link, set AC to 1
spa	/ skip on positive AC
dca A	/ overwrite A if spa fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sna	/ skip on non-zero AC
dca B	/ overwrite B if sna fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
szl	/ skip on zero link
dca C	/ overwrite C if szl fails, should not run

/ Test skips failing
cla cll cma	/ clear AC and link
spa	/ skip on positive AC
dca D	/ overwrite D if spa fails, should run
cla cll	/ clear AC and link
sna	/ skip on non-zero AC
dca E	/ overwrite E if sna fails, should run
cla cll cml	/ clear AC and link, set link to 1
szl	/ skip on zero link
dca F	/ overwrite F if szl fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 0	/ should not change
B, 0	/ should not change
C, 0	/ should not change
D, 77	/ will get 7777 when spa fails
E, 77	/ will get 0 when sna fails
F, 77	/ will get 0 when szl fails

group_2_AND_test_2.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions, AND subgroup
/ Should take 31 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test skips working first
cla cll iac	/ clear AC and link, set AC to 1
spa	sna	/ skip on positive AC, non-zero AC
dca A	/ overwrite A if spa sna fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
sna	szl	/ skip on non-zero AC, zero link
dca B	/ overwrite B if sna szl fails, should not run
cla cll iac	/ clear AC and link, set AC to 1
spa szl	/ skip on positive AC, zero link
dca C	/ overwrite C if szl fails, should not run

/ Test skips failing
cla cll cma	/ clear AC and link, load AC with 7777
spa	sna	/ skip on positive AC, non-zero AC
dca D	/ overwrite D if spa fails, should run
cla cll	/ clear AC and link
spa	sna	/ skip on positive AC, non-zero AC
dca E	/ overwrite E if spa fails, should run

cla cll	/ clear AC and link
sna	szl	/ skip on non-zero AC, zero link
dca F	/ overwrite F if sna szl fails, should run
cla cll iac cml	/ clear AC and link, set AC to 1, set link to 1
sna	szl	/ skip on non-zero AC, zero link
dca G	/ overwrite G if sna fails, should run

cla cll cml	/ clear AC and link, set link to 1
spa szl	/ skip on positive AC, skip on zero link
dca H	/ overwrite H if szl fails, should run
cla cll iac cml	/ clear AC and link, set AC to 1, set link to 1
spa szl	/ skip on positive AC, skip on zero link
dca I	/ overwrite I if szl fails, should run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 0	/ should not change
B, 0	/ should not change
C, 0	/ should not change
D, 77	/ will get 7777 when spa fails
E, 77	/ will get 0 when sna fails
F, 77	/ will get 0 when szl fails
G, 77	/ will get 1 when szl fails
H, 77	/ will get 0 when szl fails
I, 77	/ will get 1 when szl fails

group_2_AND_test_3.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions, AND subgroup
/ Should take 15 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test skips working first
cla cll iac	/ clear AC and link, set AC to 1
spa	sna szl	/ skip on positive AC, non-zero AC, zero link
dca A	/ overwrite A if spa sna fails, should not run

/ Test skips failing
cla cll cma	/ clear AC and link, set AC to 7777
spa	sna szl	/ skip on positive AC, non-zero AC, zero link
dca B	/ overwrite B if spa sna fails, should run

cla cll	/ clear AC and link
spa	sna szl	/ skip on positive AC, non-zero AC, zero link
dca C	/ overwrite C if spa sna fails, should run

cla cll iac cml	/ clear AC and link, set AC to 1, set link to 1
spa	sna szl	/ skip on positive AC, non-zero AC, zero link
dca D	/ overwrite D if spa sna fails, should not run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 0	/ should not change
B, 77	/ will get 7777 when sna fails
C, 77	/ will get 0 when szl fails
D, 77	/ will get 1 when spa fails

group_2_AND_test_4.as
/ Date : Feb 15, 2015
/
/ Desc : Tests the group 2 micro instructions, AND subgroup
/ Should take 15 cycles total
/-------------------------------------------
/ Code Section
*0200	/ start at address 0200
Main,	/ Test SKP
cla cll iac	/ clear AC and link, set AC to 1
skp	/ skip
dca A	/ overwrite A if skp fails, should not run

/ Test CLA
cla cll iac	/ clear AC and link, set AC 1
sma cla	/ skip, clear AC
dca B	/ overwrite B if sma fails, should run

cla cll	/ clear AC and link
osr	/ OR switch register with AC
dca C	/ overwrite C, should run

cla cll	iac cml	/ clear AC and link, set AC to 1, set link to 1
spa cla hlt	/ skip on positive AC, clear AC
dca D	/ overwrite D if spa sna fails, should not run
dca E	/ overwrite E if spa sna fails, should not run

hlt	/ Halt the system
jmp Main	/ In case something goes wrong
/
/ Data Section
/
*0250	/ place data at address 0250
A, 0	/ should not change
B, 77	/ will get 0 when sma fails
C, 77	/ will get OCR contents
D, 77	/ should not change
E, 77	/ should not change